## Slide 1: EEL 6246 POWER ELECTRONICS II Issa Batarseh

## Slide 2
Sign attendance sheet and/or email me that you saw this lecture.
Review Chapter 3, 4, 5 and workout the details analysis of all the isolated DC-DC Converters operating in CCM and DCM modes.
If you have not taken, EEL 5245, please send me an email to confirm the level of your understanding of the Chapters 1-5.
Assignment 1:

## Slide 3: Agenda
About the course
Syllabus Review
Course Topics
Review of Power Electronics I
Questions

## Slide 4: Introduction
CLASS SYLLABUS
Spring 2021
POWER ELECTRONICS II
EEL 6246

## Slide 5: Introduction (cont’d)
All students will be required to present their project individually in class.

## Slide 6: Introduction (cont’d)

## Slide 7: Introduction (cont’d)
Wednesday, April 28, 2021
1:00 PM – 2:00 PM

## Slide 8: What is Power Electronics?
Electronics: Solid State Electronics Devices and their Driving Circuits.
Power: Static and Dynamic Requirements for Generation, Conversion and Transmission of Power.
Control: The Steady State and Dynamic Stability of the Closed Loop system.
POWER ELECTRONICS may be defined as the application of Solid State Electronics for the Control and conversion of Power.

## Slide 9
Power Electronics as an Enabler Technology
Power electronics is considered as one of the most vibrant technology sectors due to ever increasing applications in renewable energy, computing, sensing and communication, IoT and because of its overlap with many other industry verticals.
From interfacing a mobile phone battery, hybrid cars wheels, power plant power generation and distribution to a nuclear reactor.
Require efficient power handling, from mW to GW!
To facilitate the transfer and conditioning of power from the source to the load.
To be achieved with less cost, high energy-efficiency, high power density, high reliability and neatly.

## Slide 10: Figures of Merit for Power Electronic Converters
What is the objective?
  Overall goal: To produce a converter that performs well in these areas:
    Efficiency
    Transient Response
    Load and Line Regulation
    Power Density
    Input/Output Distortion (Input Power Factor)
    Reliability (MTBF)
    Cost
  In the final analysis, the job is to process and control the flow of electric energy by supplying currents/voltages in a form most suited to both the load and energy source

## Slide 11: Modern Power Electronics
Can have efficiencies approaching 100%
  Uses switches in saturation mode (On of Off)
  On state-resistance can be down in tenths of Ohms
Are much smaller than predecessors
  High switching frequency means smaller magnetic components.
  Reduced losses means smaller package size
Net effect is better efficiency, greater power density (10’sW/in^3 attainable)

## Slide 12: Industrial Applications
Solar Energy Conversion (PV)
SMPS
PFC
Soft-Switching converters
LED Drivers
Uninterruptible Power Supplies
Motor Drives
EV and E2G and G2E
System Integration

## Slide 13: Power Electronics In terms of Fundamental Functions

## Slide 14
Power electronic systems are everywhere
Projected that by 2030, 80% of electricity could flow through power electronics at generation, storage, transmission, distribution, and end use
Figure Source: Power Electronics for Renewable and Distributed Energy Systems, Eds. S. Chakraborty, M.G. Simoes, W. Kramer; Springer 2013 (Chapter 2 – Fundamentals of Power Electronics)
Power Electronics as an Enabler Technology

## Slide 15: Historical Perspective
Traditional power conversion
  Linear Electronics- Transistors in active mode (linear region)
    Transistor acts as variable resistor for control
    Terrible efficiency (50% not uncommon)
    Low conversion range (greater Vd smaller efficiency)
    Low power applications
  Motor-Generator Sets (AC-DC or AC-AC)
    Can still be found in use
    Large physical size
    Maintenance intensive
    Low efficiency
    Poor Load regulation

## Slide 16: Simplified Block Diagram of a Power Electronics System

## Slide 17: Detailed Block Diagram of Power Electronics System

## Slide 18
Power Electronics is the Interface for technology
Power Electronics as an Enabler Technology
Controller

## Slide 19: Typical PC Power Supply

## Slide 20: Multidisciplinary Nature of Power Electronics
Power electronics is comprised of:
      Semiconductor Devices
      Analog Circuits
      Control Design
      Magnetics
      Electric Machines
      Power Systems Engineering
      Circuit Simulation

## Slide 21: Power Electronics Focus Areas

## Slide 22: Power Conversion Dictates Change in Current and/or Voltage:
    Voltage/Current form ac or dc
    Voltage/Current level (magnitude)
    Voltage frequency (line or otherwise)
    Voltage/Current waveshape (sinusoidal or nonsinusoidal such as square, triangle, sawtooth, etc.)
    Voltage phase(single or three-phase).

## Slide 23: Conversion Type Description
Power Electronic systems perform one or more of the following conversion functions:
a)Rectification (ac-to-dc)
b) Inversion (dc-to-ac)
c) Cycloconversion
(ac-to-ac different frequencies) or
(ac-to-ac same frequency)
d) Conversion (dc-to-dc)

## Slide 24: Over All Block Diagram
Definition of Power Electronics
Industry Overview and Market Share Analysis
Multidisciplinary Nature of the Field
Block Diagrams of Power Electronic Systems
The Need for Power Electronics
Types of Power Conversion
Need for Control
Figures of Merit for Power Electronic Converters
Future Trends

## Slide 25: Typical PC Power Supply

## Slide 26: Power Flow Unidirectional: input-to-output

## Slide 27: Power Flow – Bi-directional

## Slide 28: Course Content Overview: Non-isolated DC-DC Converters Continuous Conduction Mode (CCM)
Principles of Steady State Converter Analysis
  Definition of Steady State
  Inductor Volt-Second Balance
  Capacitor Charge Balance
  Small Ripple Approximation
  Average Values in Steady State
  Use of Power Conservation Principle in Converter Analysis
Application of Analysis Techniques to Classic Converter Topologies
  Buck, Boost, and Buck Boost
Analysis of Fourth Order Converters

## Slide 29: Course Content Overview: Non-isolated DC-DC Converters Discontinuous Conduction Mode (DCM)
Description of DCM
At what operating condition does DCM occur?
Application of Steady State Analysis Principles to Converters in DCM
  Buck
  Boost
  Buck-Boost
  Cuk
Properties of Converters in DCM

## Slide 30: Classic Inverter Scheme

## Slide 31: Course Content Overview: Switching Concepts
The Need for Switching in Power Electronic Circuits
Efficiency Example Comparing Power Supply Designs
Ideal Switch Discussion
Ideal Switch Types
Practical Switch Characteristics

## Slide 32: Course Content Overview: Semiconductor Device Overview
Discussion of Available Power Semiconductor Devices
  Power Diode
  BJT
  Power MOSFET
  IGBT
  SCR
  GTO
  TRIAC
Focus on Device i-v Characteristics
Comparison of Switching Devices
Survey of Commercially Available Devices
Future Trends

## Slide 33: Ideal Switch Characteristics
Zero on-state resistance
  No forward voltage drop when on
Infinite off-state resistance
  No leakage current when off
Current limitless when on-either direction
  Conduction current a function of external components only
No limit on amount of voltage across switch when off
  Blocking voltage infinite (forward or reverse)
Switch can transition from on-off or off-on instantaneously when commanded to

## Slide 34: Ideal Switch i-v Characteristics (Transition)
Previous desirable conditions mean, no power loss by any mechanism (conduction, leakage, or switching)
  Switch transition-No overlap
  Von=0V, Ioff=0A

## Slide 35: Practical Switch
Although Semiconductor Industry has produced amazing devices, the “real world” switch is not ideal
  Limited conduction current when the switch on, limited blocking voltage when the switch is in the off
    Both are directional in practical switch
  Limited switching speed that caused by the finite turn-on and turn-off times
    Real world (Semiconductor) switches are charge driven
  Finite, nonzero on-state and off-state resistances
    There is a I^2R loss when on and some leakage when off (very small)

## Slide 36: Practical Switch i-v Characteristics (Transition)
This is root cause of the single major source of loss in PE converters
  Conduction- When switch is in on state (off state too, to a lesser degree)
  Switching Losses- When switch is transitioning from on to off or off to on

## Slide 37: Theoretical Efficiency Example
We’ll do an example to underscore why switching is the most energy efficient choice
Consider the design of a DC-DC converter as shown above
Design requires 24V step down to 12V across a 6 Ohm resistive load
Let’s investigate, some possible options

## Slide 38: Theoretical Efficiency Example Voltage Divider
A simple voltage divider can do job
R must be set to 6 Ω
Load cannot change-R fixed so no opportunity for control
Losses are high η=50%

## Slide 39: Theoretical Efficiency Example Zener Regulator
Need some control (regulation)
A Zener Regulator will allow for load variation
Assume Vz=12V, Iz@12V=.2A , Rdrop=5.5Ω
Pin=Pout+Prdrop+Pzener=24W+26.2W+2.4W=52.6W
η=46%

## Slide 40: Theoretical Efficiency Example Linear Regulator
Drop resistor inefficient means
Direct source connection is preferable
Try linear regulator
  (Similar to implementation 7805, LM317 etc.
Assume Vce=12V
Pin=Pout+Pnpnloss=24W+24W=50W
η=50%

## Slide 41: Theoretical Efficiency Example Duty Ratio Controlled Switch
Instead of operating transistor in active mode try using as switch
Low Pass filter required to extract DC
η=100%

## Slide 42: Circuit Implementation Duty Ratio Controlled Switch-SPDT

## Slide 43: DC Component

## Slide 44: Step Down Converter-Buck
Low Pass extracts DC
Position 2 allows for current “freewheeling”
Vo can be controlled by adjusting D (Switching Period/Frequency Fixed), Vo/Vin = D
Ideally, is no switch/filter loss, η=100%
  We assume an ideal switch here

## Slide 45: Buck Converter
Switch Position 2 for allow for uninterrupted inductor current flow
LPF for smoothing of pulse for constant DC output
Capacitor hold a DC value for the load when switch in position 1 (Inductor current charge)
2nd Order-1 L, 1 C

## Slide 46: Derivation of Classic Converter Topologies (2nd Order)

## Slide 47: Classic Converter Topologies

## Slide 48: Analysis of Classic Converter Topologies
Analysis will assume lossless components
Exact steady state analysis would involve solution of nonlinear, 2nd Order system, we will simplify to a 1st Order System with:
  Since RC>>Ts, output voltage nearly constant over switching period
    Since ripple is assumed small, we assume Vo a constant during analysis (output cap not considered)
We assume analysis of converter takes place at after it has reached steady state
  Since steady state, average inductor voltage equals zero over switching interval (volt-sec balance)
  Since steady state, average capacitor current over one switching interval equals zero (charge balance)

## Slide 49: Analysis of Classic Converter Topologies
The preceding concepts can be expressed in terms of mathematical relations.
These are tools for analysis:
  Pout=Pin (Power Conservation)
  iL(to)=iL(to+Ts) (Steady State)
  Icavg=0 (Charge Balance)
  VLavg=0 (volt-sec balance)

## Slide 50: Converter Analysis Principle Small Ripple Approximation

## Slide 51: Converter Analysis Principle Inductor Volt-Second Balance
Inductor defining relation :
Integrate over one complete switching period :
In periodic steady state, the net change in inductor current is zero :
Hence, the total area (or volt-seconds) under the inductor voltage
waveform is zero whenever the converter operates in steady state.
An equivalent form:
The average inductor voltage is zero in steady state

## Slide 52: Converter Analysis Principle Volt-Second Balance gives Voltage Gain, M
Example is for Buck

## Slide 53: Converter Analysis Principle Capacitor Charge Balance
Capacitor defining relation:
Integrate over one complete switching period
In periodic steady state, the net change in capacitor voltage is zero:
Hence, the area (or charge) under the capacitor current
waveform is zero whenever the converter operates in steady state.
The average capacitor current is then zero.