## Slide 1: EEL 5245 POWER ELECTRONICS I Lecture #15 Ch 4: Non-Isolated DC-DC Converters Boost and Buck Boost Analysis (CCM)

## Slide 2: Objectives
Boost and Buck-Boost Converter Analysis (CCM)
  Voltage Conversion Ratio (M=Gain)
  Average Input and Output Currents
  Output Voltage Ripple via Charge approximation
  Boundary Between CCM and DCM
iPES Examples for Boost CCM
Calculation Example
Analysis Verification by Simulation

## Slide 3: Figures of Merit for the PWM DC-DC Converter “Plan of Attack”
Classic Converter Analysis (CCM)
  Voltage Conversion Ratio (M=Gain)
    Use Inductor Volt-second balance
  Average Input and Output Currents
    Use waveform analysis and
    Capacitor charge balance and small ripple approximation (Icavg=0)
  Output Voltage Ripple via Charge approximation
    Small ripple approximation means all ac component of output current seen by capacitor, DC to load R
  Inductor current Ripple
    Derived from inductor current waveform
  Boundary Between CCM and DCM
    Concept of Critical Inductance derived from iL expressions

## Slide 4: Boost Converter Analysis (Step Up)
Boost Converter w/ Ideal Switch
Boost Converter realized w/ MOSFET

## Slide 5: Boost Converter Analysis Circuit Modes

## Slide 6: Boost Converter Analysis Circuit Mode I
Inductor Voltage and Capacitor Current

## Slide 7: Boost Converter Analysis Circuit Mode II
Inductor Voltage and Capacitor Current

## Slide 8: Boost Converter Analysis Inductor Voltage and Capacitor Current
Mode I
Mode II

## Slide 9: Boost Converter Analysis Inductor Voltage Second Balance
Net volt-seconds applied to inductor over one switching period:
Set equal to zero and solve:

## Slide 10: Boost Converter Analysis Voltage Conversion Ratio

## Slide 11: Boost Converter Analysis: Hand Calculation Example 4.4
Example 4.4
Sketch all waveforms for a boost converter with the following
circuit parameters: Vin = 50V, Vo= 120V and R= 20, fs = 15kHz, L=1.8mH, C=147μF

## Slide 12: Boost Converter Analysis: Hand Calculation Example 4.4
Ilmax=14.937
Ilmin=13.863
Iinavg=14.4
Ioavg=6

## Slide 13: Boost Converter Analysis: Hand Calculation Example 4.4
Icmax=14.937-6=8.937
Icmin=13.863-6=7.863

## Slide 14: Boost Converter Analysis: Simulation Verification Example 4.4

## Slide 15: Boost Converter Analysis: Simulation Verification Example 4.4-Startup
Time
0s
10ms
20ms
30ms
40ms
50ms
V(Output)
I(L)
0
100
200
Vout=120 V
ILAve=14.4A

## Slide 16: Boost Converter Analysis: Simulation Verification Example 4.4-Startup
Time
0s
10ms
20ms
30ms
40ms
50ms
V(Output)
I(L)
0
100
200
Vout=120 V
ILAve=14.4A

## Slide 17: Boost Converter Analysis: Simulation Verification Example 4.4-Inductor Current/Voltage
Time
34.80ms
34.85ms
34.90ms
34.95ms
I(L)
14.0A
14.5A
15.0A
(34.841m,15.004)
(34.935m,13.918)
Time
34.80ms
34.85ms
34.90ms
34.95ms
V(L:1,L:2)
-50V
0V
50V
-80V

## Slide 18: Boost Converter Analysis: Simulation Verification Example 4.4-Capacitor Current/Voltage
Time
34.80ms
34.85ms
34.90ms
34.95ms
V(Output)
119V
120V
121V
Time
34.80ms
34.85ms
34.90ms
34.95ms
I(Cf)
-5A
0A
5A
10A
(34.842m,8.9882)
(34.868m,7.8893)

## Slide 19: Buck-Boost Converter Analysis (Step Up/Down)
Boost Converter w/ Ideal Switch
Boost Converter realized diode/BJT

## Slide 20: Buck-Boost Converter Analysis (Step Up/Down)
Steady State Analysis
Mode I – The main switch is ON and D is OFF
Mode II – The main switch is OFF and D is ON

## Slide 21
Detailed Steady-State Analysis

## Slide 24
Buck Converter Analysis: Waveforms

## Slide 26
Buck Converter Analysis: Voltage Gain

## Slide 27
Buck Converter Analysis: CCM Vs. DCD

## Slide 28: Buck-Boost Converter Analysis (Step Up/Down- Summary)

## Slide 29: Buck-Boost Converter Analysis (Step Up/Down)

## Slide 30: Buck-Boost Converter Analysis (Step Up/Down)

## Slide 31: Buck-Boost Converter Analysis (Step Up/Down)
2

## Slide 32
Example: Given the following switching waveforms where q(t) is the driving waveform of the main switch.
(a) Sketch the topology, (b) Find L
vL: Voltage across the inductor
iL: Current through the inductor
idiode: Diode current
iC: Output capacitor current
(c) Find Vo, Vin, fs and Po
Vo: Output Voltage
Vin: Input Voltage
fs: Switching frequency
Po: Output power

## Slide 33
Solution: The Buck Boost Circuits is drown bellow.
Buck-Boost
L=26.25 uH,
Vin=14V,
Vo=42V,
Po=21W
Inductor Ripple=2A
and fs=200kHz
Solutions:
Recall, in the Buck Circuit:

## Slide 34
Solution: The Buck Boost Circuits is drown bellow.
Solutions:
Recall, in the Buck Circuit:
Recall, in the Boost Circuit:
Recall, in the Buck-Boost Circuit:

## Slide 35
Solution: The Buck Boost Circuits is drown bellow.
Solutions:
Recall, in the Buck Circuit:
Recall, in the Boost Circuit:
Recall, in the Buck-Boost Circuit:

## Slide 36
Solution: The Buck Boost Circuits is drown bellow.
Buck-Boost
L=26.25 uH,
Vin=14V,
Vo=42V,
Po=21W
Inductor Ripple=2A
and fs=200kHz
Solutions:
The Buck Boost Circuits is drown bellow.