## Slide 1: EEL 3004 Electrical Networks Lecture #22 Reactive and Complex Power

## Slide 2: Announcements
Final Exam
Topics: Comprehensive
Final Exam – Tuesday April 21, 2020
1-3:50 PM Online
H.W. # 8
Topics: Power Calculations
Due April 12.
Quiz # 5
Topic: Power Calculations – H.W. #8 and Lectures 21 and 22
Will be online during our next lecture: Tuesday April 14

## Slide 3: Lecture Objectives
The lecture today will introduce these new power quantities:
Reactive Power
Complex power
Apparent power

## Slide 4: Lecture Objectives
Chapter 9
Power Analysis in AC circuits
Chapter Outlines
Introduction
9.1 Instantaneous Power
9.2 Average Power
9.3 Reactive Power/Complex Power
9.4 Complex Power
9.5 Power Factor

## Slide 5
Reactive Power is the power that gets exchanged back and forth in reactive elements; inductors and capacitors.
The power quantity for the Reactive Power is denoted by Q.
Q is expressed in the instantaneous power delivered to a general RLC network driven by sinusoidal v(t) and i(t) and given by,
Reactive Power
Recall that the instantaneous power is given by,

## Slide 6
Reactive Power
Recall that the instantaneous power is given by,
It can be shown that the instantaneous power can be rewritten as,
Where Pave is the average power being delivered to the network, and Q is the reactive power being stored is the reactive elements.
where,
Fixed quantalities

## Slide 7
To distinguish the average power and the reactive power, we use watts (W) for instantaneous and average (real) power
Reactive Power
When Q is positive then the circuit is inductive and when Q is negative then the circuit is capacitive
Watts (W)
Where as Q is given as the product of volt (V) and amp (I) for reactive power (R) for reactive power – (VAR)
VAR

## Slide 8
Having defined Q, the instantaneous power expressions Pav for capacitors and inductors can be expressed in terms of Q,
So the measure of the power associated with an inductor and capacitor is the reactive power Q.
Q represents the average amount of power that gets exchanged between the source and the rest of the circuit.
Pav represents the measure of the power associated with a resistor.
Reactive Power

## Slide 9
Reactive power In the inductor
Recall that the reactive power in any circuit with any sinusoidal voltage and current functions is given by,
For the inductor,
Then the Reactive Power in the inductor ,
Since

## Slide 10
Current lags voltage by in the inductor

## Slide 11
Reactive power In the inductor
=
Since we have,
Recall that the reactive power in any circuit with is given by,
For the capacitor,
Then the Reactive Power in the capacitor,

## Slide 12
Current leads voltage by in the capacitor

## Slide 13
Example
(a) Determine the reactive power supplied to the load between terminals “a” and “b” for the circuit with source voltage,
(b) Determine the individual element reactive power.
(c) Show that the total VARs generated by the source are equal to the total VARs in the reactive elements.

## Slide 14
The phasor equivalent circuit is shown,
The total equivalent impedance of the circuit is given by,
Where,
First we need to find the phasor current .

## Slide 15
Now, the resulting phasor current drawn by the source is given by,
So, is given by,
A
A
The corresponding time domain

## Slide 16
The reactive power at the terminals “ab” is equal to the reactive power supplied by the voltage source and it is given by,
The resistor in the load doesn’t absorb or generate any reactive power.
The only reactive elements in the circuit are the inductor and capacitor.
So, the 9.5 VARs are disrupted across C and L.
VAR
VARs

## Slide 17
The reactive power absorbed in the inductor is given by (since is also the inductor current)
The reactive power absorbed in the capacitor is given by,

## Slide 18
The total VARs absorbed in the load is given by,
It can be seen that the total supplied VARs (QSUP) is equal to the absorbed VARs in both the inductor and the capacitor (QLC).
=9.5
The average power dissipated across R is given by,

## Slide 19
Let us check the answers from the time domain instantaneous power.
=9.5
The average power dissipated across R - W
We have the following time domain voltage and current:
The time domain instantaneous power is given by.
W

## Slide 20
Another way to express the time-domain instantaneous power.
=9.5
where,
As obtained from the phasor analysis

## Slide 21
t(ms)
V
=

## Slide 22
A
t(ms)
(A)
=

## Slide 25
Negative power

## Slide 26
=
Negative power

## Slide 27
Let us find the maximum/minimum power theoretically,
We take the 1st derivative and set it to 0 and solve for the time when this occurs.
Assume this time is .
Then the maximum is given by,
Then the minimum power occurs at the time of half of the power period later,

## Slide 28
What happens if we let the phase angle of be zero, i.e.
This means the phase angle of is the same as the phase angle of as follows,
This means the total Q supplied by the circuit is zero,
This means the circuit has only real power supplied by the source.
This means the real power (average) is at its maximum value:
This means
(

## Slide 29
Let us re-design the values to make .
Recall,
For , we need to have,
In our case we have,
For the redesigned ,
Since is fixed we need to re-design L or C. Let us design a new value for C.

## Slide 30
Now, the resulting phasor current drawn by the source is given by,
The corresponding time domain iS(t),
So, is given by,
A
A
VAR
The reactive power absorbed in the inductor is given by,
The reactive power absorbed in the capacitor is given by,

## Slide 31
The instantaneous power is given by,
(No negative power)

## Slide 32
t(ms)
(V)
=

## Slide 33
A
t(ms)
(A)
=

## Slide 34
and current are in-phase

## Slide 35
and current are in-phase

## Slide 37
NO Negative power

## Slide 38
Complex power contains all the relevant information needed to calculate power delivered to the load, denoted by S, and defined as,
The real part of S is the exactly equal to the average power, and the imaginary part of S is exactly equal to the reactive power.
Substituting for Pave and Q, yields,
(
Complex Power (S)

## Slide 39
Representing the voltage and current peak values by their equivalent rms values,
S is expressed as,
Where,
Where denotes the complex conjugate of the phases current .
Complex Power (S)

## Slide 40
Complex Power (S)
To distinguish between power quantities Pave, Q and S, which are all products of voltage and current, the dimension for S is measured in volt-amp (VA).
The magnitude of S is given by,
|
And the phase angle of S is given by,

## Slide 41
The magnitude of complex power, |S|, is referred to as apparent power measured in volt-amp (VA).
Apparent power represents the maximum average power that can be delivered to the load.
Maximum average power that equals to the apparent power can only occur when,
Which results in,
This occurs when the load is purely resistive with zero shift between voltage and current.
Apparent Power

## Slide 42
Another useful relation for Pave, Q and S, is to use the load representation.
If we represent the load circuit by a total impedance ZLoad given by,
where the real part R is the effective resistive component of the load, and the imaginary part X is the reactive component of the load.
Load Impedance Point of View

## Slide 43
Pave, Q and S, can be represented using the load impedance.
Phasor rms voltage and current values are related in terms of ZLoad as,
Substituting into S yields,
Hence, as expected Pave and Q are only dependent on resistive and inductive values, respectively,
Load Impedance

## Slide 45
Example
Consider the circuit with a voltage source feeding a single load impedance ZL.
Given the following: * The average power – Pavg= 5 W
* The loads phase - ZL=
* The loads peak voltage -|VL|=10 V
* The transmission line impedance - ZLine = 0.2 + j 0.5 Ω.
Determine:
The magnitude of the load impedance
The reactive, apparent and complex power delivered to the load,
Time-domain and phasor domain expressions for iS(t) and vS(t).
Assume =100 rad/s

## Slide 46
The equivalent phasor circuit is given by,
The magnitude of the load impedance can be found as follows,
Solution:

## Slide 47
The reactive power in the load is given by,
The apparent power at the load is given by,
The complex power at the load is given by,

## Slide 48
The load current IL is equal to the source current IS, and is given by,
Assuming the load voltage to be the reference (0 phase),

## Slide 49
The transmission line current is also equal to the load current IL,
The transmission line impedance is given by,
Now, the transmission line voltage is given by,

## Slide 50
We can now obtain the source voltage by applying KVL around the loop,
After finding both VS and IS, their phase difference is given by,

## Slide 51
The corresponding time domain for vS(t) and iS(t) is given by,

## Slide 52
For the given the two parallel impedance loads,
The average , reactive and complex power , for each passive element in addition to the source.
And show that , and are all conserved.
Example
Ω
Connected to a voltage source as shown.
Determine:

## Slide 53
Solution
The voltage across the parallel load is given as , therefore the average power in is given by,
W
The reactive power in is given by,
VAR
The complex power in is given by
VA
VA

## Slide 54
Similarly, we can find the average power values in . First, the average power is given by,
The reactive power in is given by,
The complex power in is given by
W
VAR
VA
VA

## Slide 55
To find all the power quantities, we need to find the main current .
Now, the current is given by,
A
Now, the current is given by,
A
The current is given by,

## Slide 56
The total average power at the source is given by,
W
The total reactive power for is given by,
VAR
The complex power for is given by
VA

## Slide 57
Notice the conservation of the all the power quantities
In the load impedance
In the load impedance
From the main source
W
W
W
VAR
VAR
VAR
VA
VA
You can show that
VA