## Slide 1: EEL 3004 Linear Circuits I Lecture #4 KVL and KCL Laws

## Slide 2: Lecture Objectives
To understand and apply the following laws:
  Kirchhoff's Voltage Law (KVL)
  Kirchhoff's Current Law (KL)
Be able to combine resistors that are in:
  Resistors in Series
  Resistors in Parallel

## Slide 3: Kirchoff’s Voltage Law
The algebraic sum of all voltages in a closed circuit is equal to zero.
(KVL is a law of conservation of energy (zero net change in energy).
Where: Vn is the voltage across branch n.
Apply KVL around the loop:
Mathematically, KVL can be written more compactly as follows,
where,
is the voltage of the element for .
Closed circuit - Loop

## Slide 4: Kirchoff’s Voltage Law
Voltage source (Excitation) - between nodes a and a’
Resistance R1 between nodes b and b'
Resistance R2 between nodes c and c'
KVL:
Example of four elements
In terms of voltages assigned across the elements:

## Slide 5: Kirchoff’s Voltage Law
What about if we apply KVL by looking at the node voltages?
Example of four elements
But we have:

## Slide 6: Kirchoff’s Voltage Law - Example
KVL:
Example of
six elements

## Slide 7: Kirchoff’s Voltage Law
Closed loop
Element Voltages:
The voltage across elements like Vx ,Vy,Vz V1,V2
-V1+Vx+Vy+Vz -V2=0
Apply KVL

## Slide 8: Kirchoff’s Voltage Law
Closed loop
Element Voltages:
The voltage across elements like Vx ,Vy,Vz V1,V2
-V1+Vx+Vy+Vz -V2=0
Apply KVL
What about the voltage at Va ?
What about the voltage at Vb ?
Undetermined! Unknown! Invalid Question!

## Slide 9: Kirchoff’s Voltage Law
Closed loop
Node Voltages:
The voltage at Va or at Vb must be in measured with respect to another node voltage or to the ground?
Let us find the voltage between nodes Va or at Vb

## Slide 10: Kirchoff’s Voltage Law
Closed loop
Node Voltages:
The voltage at Va or at Vb must be in measured with respect to another node voltage or to the ground?
Let us find the voltage between nodes Va or at Vb
Two options:
Go around to the clockwise direction
Go around in the counter clockwise
direction

## Slide 11: Kirchoff’s Voltage Law
Closed loop
Node Voltages: The voltage between two nodes can be obtained by adding all voltages along the path that connects the two nodes.
Va-Vb = V1+V2
OR
Va-Vb = Vx+Vy+Vz

## Slide 12: Example
Given the circuit, apply KVL to find the current i.
Simple electric circuit
Variable | Values | Unit
V | 14 | V
R1 | 15 | Ω
R2 | 20 | Ω

## Slide 13: Example
Simple electric circuit
Solution:
From KVL,
Starting from node
Solving for current i by using Ohm’s Law,
First assign voltage polarities:

## Slide 14
Example
Given the circuit shown, apply KVL to find:
The current
The voltage .
 | Default | 
Variables | Values | Unit
R1 | 15 | Ω
R2 | 5 | Ω
R3 | 8 | Ω
R4 | 4 | Ω
V | 25 | V

## Slide 15
Solution A - clockwise direction:
First we need to find
Assign voltage as shown
Apply KVL equation moving in the clockwise direction:
From Ohm’s law
Solve for :

## Slide 16
Next, to find , KVL can be applied around the path V and as shown
Solving for ,
Apply KVL equation:
Solution A - clockwise direction:

## Slide 17
Solution B – counter clockwise direction:
First we assign voltage as shown
Apply KVL equation moving in the counter clockwise direction:
From Ohm’s law
Solve for :

## Slide 18
Next, to find , KVL can be applied around the path V and as shown
Solving for ,
Apply KVL equation moving counter clockwise direction:
Solution B – counter clockwise direction:

## Slide 19
To find , KVL can be applied around the path , as shown
Apply KVL equation:
Solution C – Different portion of the circuit:

## Slide 20
To find , KVL can be applied around the path , as shown
Apply KVL equation:
Solution C – Different portion of the circuit:

## Slide 21: Example
Circuit with voltages and
Variable | Values | Unit
V1 | 28 | V
V2 | 14 | V
R1 | 18 | Ω
R2 | 13 | Ω
R3 | 15 | Ω
R4 | 12 | Ω
Given the circuit, apply KVL to find the voltages vx and vy.
Example

## Slide 22
Example
Solution:
First we need to calculate the current i using KVL,
Using Ohm’s Law and solving for i,
Circuit with voltages and

## Slide 23: Example
Solving for voltage vx
Solving for vx:
Applying KVL around the path d-d', e-e', f-f', and f'-a' as shown,
Using Ohm’s Law and solving for vx,

## Slide 24: Example
Solving for voltage vy
Solving for vy :
Applying KVL around the path c-c', d-d', and d'-c as shown
Using Ohm’s Law and solving for vy,

## Slide 25
Kirchhoff's Current Law
The sum of all currents i1, i2, …in at any node is equal to 0.
Mathematically, KCL is given by,
is the current of the element for .

## Slide 26: Kirchhoff’s Current Law
OR
The total currents flowing in = total currents flowing out.
I1+I4+I5=I2+I3
I+5=3+4+2
I= 4 A
OR

## Slide 27: Kirchoff’s Current Law
The three branches:
Current source (Exciting Force) between nodes a and a’
Resistance R1 between nodes b and b’
Resistance R2 between nodes c and c'
KCL @ upper node: I=iR1 + iR2 or I- iR1 - iR2 =0
Upper node
Lower node
KCL @ lower node: I=iR1 + iR2 or -I+ iR1 + iR2 =0
Example:

## Slide 28: Example
Simple electric circuit
Variable | Values | Unit
I | 1 | mA
R1 | 5 | kΩ
R2 | 3 | kΩ
R3 | 4 | kΩ
Given the circuit, apply KCL to find the current iR2.
Example

## Slide 29: Example
Simple electric circuit
Solving for current iR2 using Ohm’s Law,
Solution:
Assign currents and voltages.
Applying KCL at node “A”,
Voltage across all resistors is equal,
Solving for voltage v,

## Slide 30: Example
Given the circuit, apply KCL to find the voltage v.
Resistive circuit
Variable | Values | Unit
I1 | 1 | mA
I2 | 2 | mA
R1 | 1 | kΩ
R2 | 2 | kΩ
g | 0.8 | 1/kΩ
Example

## Slide 31: Example
Resistive circuit
Solution:
It can be seen by Ohm’s Law that
From Ohm’s Law we deduct,
Applying KCL at node ‘A’,

## Slide 32: Example (Con’d)
Resistive circuit
Substituting in the KCL equation,
Solving for v,
- 1.43V

## Slide 33: Kirchoff’s Current Law
KCL also extends to surfaces of planar circuits.
KCL is a statement of conversation of charge, i.e., no charge is being generated or destroyed as a result of current flow.

## Slide 34
Example :
Find and the power absorbed or delivered by each element. Then check that the conservation of power law is satisfied.
Variable | Default | Unit
I | 6 | A
V | 12 | V
 | 2 | A
Variable | Default | Unit
I | 6 | A
V | 12 | V
 | 2 | A

## Slide 35
Solution:
The current source I=6A supply the amount of power given by,
The current is obtained by applying KCL at the upper node as follows,
Solving for ,
So, the power absorbed by element 1 is given by,
And the power absorbed in element 2,
The total power generated or supplied is 72W and the total power absorbed is 48W+24W=72W, making the conservation of power applied.

## Slide 36
Variable | Value | Unit
I | 6 | A
V1 | 12 | V
V2 | 12 | V
V3 | 3 | V
Vi | 9 | V
 | 2 | A
Variable | Value | Unit
I | 6 | A
V1 | 12 | V
V2 | 12 | V
V3 | 3 | V
Vi | 9 | V
 | 2 | A
Example:
Find and the power absorbed or delivered by each element. Then check that the conservation of power is satisfied.

## Slide 37
Solution:
The current source I=6A supplies the amount of power given by,
The element 3 supplies the amount of power given by,
The current is obtained by applying KCL at the upper node as follows,
Solving for ,
So, the power absorbed by element 1 is given by,
And the power absorbed in element 2,
The total power generated or supplied is 54W+18W=72W and the total power absorbed is 48W+24W=72W, satisfying the conservation of power requirement.

## Slide 38
Variable | Default | Unit
I | 6 | A
V1 | 9 | V
Vi | 12 | V
V3 | 3 | V
V2 | 12 | V
iy | 2 | A
Example:
Find and the power absorbed or delivered by each element. Then check that the conservation of power is satisfied.

## Slide 39
Solution:
The current source I=6A supplies the amount of power given by,
The current is obtained by applying KCL at the upper node as follows,
Solving for ,
So, the power absorbed by element 1 is given by,
And the power absorbed in element 2,
The element 3 absorbs the amount of power given by,
The total power generated or supplied is 72W and the total power absorbed is 36W+24W+12W=72W, satisfying the conservation of power requirement.

## Slide 40
Variable | Default | Unit
I | 6 | A
V1 | 9 | V
V2 | 9 | V
V3 | 3 | V
V4 | 3 | V
Vi | 12 | V
iy | 2 | A
Example:
Find and the power absorbed or delivered by each element. Then check that the conservation of power is satisfied.

## Slide 41
Solution:
The current source I=6A supplies the amount of power given by,
The current is obtained by applying KCL at the upper node as follows,
Solving for ,
So, the power absorbed by element 1 is given by,
And the power absorbed in element 2,
The element 3 absorbs the amount of power given by,
The element 4 absorbs the amount of power given by,
The total power generated or supplied is 72W and the total power absorbed is 36W+18W+12W+6W=72W, satisfying the conservation of power requirement.

## Slide 42: Resistors in Series
Resistors in Series
Resistors in Series:
Each of the two elements are connected to the same node without any additional elements connected to that node.
The current entering the first element equals the current entering the second element.

## Slide 43: Example
Consider the circuit shown, apply Ohm’s and Kirchoff’s voltage laws to find the equivalent resistor seen by the voltage source.
Variable | Values | Unit
V | 15 | V
R1 | 1 | kΩ
R2 | 2 | kΩ
Resistors in Series

## Slide 44: Example
Solution:
From Ohm’s Law,
Applying KVL around the loop,
Substituting for the resistor voltage,
Therefore,
Resistors in Series
The total resistance seen by the voltage source V

## Slide 45: Example
Consider the circuit shown, apply Ohm’s and Kirchoff’s voltage laws to find an expression for the equivalent resistor seen by the voltage source.
Solution:
From Ohm’s Law,
Applying KVL around the loop,
Resistors in Series

## Slide 46: Example
From Ohm’s Law,
Rearranging the equation gives,
Therefore,
The total resistance seen by the voltage source V

## Slide 47: Resistors in Parallel
Resistors in Parallel
Resistors in Parallel:
  Both ends of one element are connected to both ends of the other element.
  The voltage across the first element equals the voltage across the second element.

## Slide 48: Example
Consider the circuit shown, find the total resistance seen by the current source by applying Ohm’s and Kirchhoff's voltage laws.
Values:
Variable | Default | Unit
I | 10 | mA
R1 | 2.5 | kΩ
R2 | 2.5 | kΩ
R3 | 1.25 | kΩ
Resistors in Parallel

## Slide 49: Example
Consider the circuit shown, find the total resistance seen by the current source by applying Ohm’s and Kirchhoff's voltage laws.
Values:
Variable | Default | Unit
I | 10 | mA
R1 | 2.5 | kΩ
R2 | 2.5 | kΩ
R3 | 1.25 | kΩ
Resistors in Parallel

## Slide 50: Example
Solution:
From Ohm’s Law,
Since the resistors are in parallel,
Applying KCL at the top node,
Resistors in Parallel

## Slide 51: Example
Substituting for the resistors currents from the above equations,
Therefore,
Resistors in Parallel
The total resistance seen by the current source I

## Slide 52: Example
Consider the circuit shown, apply Ohm’s and Kirchoff’s voltage laws to find an expression for the equivalent resistor seen by the current source.
Solution:
From Ohm’s Law,
Resistors in Parallel

## Slide 53: Example
Since all elements are connected in parallel,
Applying KCL at node v,
Applying Ohm’s Law to the equation yields,

## Slide 54: Example
Rearranging the equation yields,
Therefore,

## Slide 55: Resistors in Series and Parallel
Not all resistors in a circuit can be connected in series or parallel
Resistor connections that cannot be combined

## Slide 56: Example
Consider the circuit shown, find the main current i being supplied by the voltage source.
Values:
Variable | Default | Unit
V | 15 | v
R1 | 1 | Ω
R2 | 4 | Ω
R3 | 4 | Ω
Simple resistive circuit

## Slide 57: Example
Solution:
The equivalent resistance as seen from terminals “ab” is shown,
Equivalent resistance

## Slide 58: Example
The circuit shows the equivalent circuit after replacing the three resistors R1, R2 and R3 with one resistor Req,
Apply Ohm’s law and solving for the current gives,
Equivalent Resistance

## Slide 59: Example
Equivalent Resistance
Consider the circuit shown, find the main current i being supplied by the voltage source.
=
]

## Slide 60: Example
Equivalent Resistance
Consider the circuit shown, find the main current i being supplied by the voltage source.
Solving for the current to give,

## Slide 61: Example
Determine:
The total power dissipated in the resistors
Determine
The total power supplied or dissipated in the dependent source
Verify the conservation of power concept
In the circuit shown, the independent source delivers input power to the circuit. Assume , , and .

## Slide 62: Example
The input power supplied by the independent voltage source is given by,
Solving for
Solution:
The Network

## Slide 63: Solution
The current in as labeled is obtained by applying KCL at the node connecting the three resistors as follows,
The voltage across is given by,
The power absorbed in is given by,

## Slide 64: Solution
The voltage across is obtained from KVL when applied to the left loop,
(b) Therefor, the resistor value of is given by,
The power absorbed in of the left loop is given,

## Slide 65: Solution
The power absorbed in of the right loop is given by,
Where is given by,
So, the power absorbed in of the right loop is given by,
The total power dissipated in the three resistors is,

## Slide 66: Solution
(b) The power delivered to the dependent limit source is given by,
Where,
Therefore, power delivered to the dependent limit source is given by,
(d) The conservation of power is given by,
As expected!

## Slide 67
Example - Power and Energy
If in a certain residential application, a 36 V battery can supply 7 kW power continuously for one hour at 2.5 A. This means the battery capacity is 7 kWh.
(a) What is the battery capacity rating in Ampere-Hours (Ah)?
(b) If battery is fully charged, how long will the house continued to be powered by the battery?
(c) How much energy in joules did the house consume when using fully charge battery?

## Slide 68
Example - Power and Energy
Solution:
The energy capacity in can be expressed as,
1
Therefore, the expression for is given by,

## Slide 69
Example - Power and Energy
Solution:
In this problem we have states that battery can supply 7 kW power continuously for one hour : so  7kW-hour = 7kWh
and voltage=36 V, hence

## Slide 70
Example - Power and Energy
Solution:
(b) We have Ampere-hour rating (Ah) and since the average current I supplied to the load from battery, therefore,

## Slide 71
Example - Power and Energy
Solution:
(c) Fully charge battery has rated capacity of 7 kWh
1 kWh = 3600000 joules =3.6 Mjoules
Therefore, for 7 kWh battery joules consumed by house will be,