## Slide 1: EEL 3004 Electrical Networks Lecture #6 Simple Circuit Analysis Voltage and Current Division Formulas & Delta and Wye Connection

## Slide 2: Simple Circuit Analysis Techniques
Chapter Three
Chapter Outline
Introduction
3.1 Analysis of Single-Loop Circuits
3.2 Analysis of Single-Node-Pair Circuits
3.3 Voltage and Current Division
3.4 Intuitive Analysis Method: Circuit Reduction
3.5 Voltage and Current Source Transformation

## Slide 3: Lecture Objectives
The lecture today will focus on Sections 3.3 and 3.4:
* Present two simple, but important, formulas:
  Voltage Division
  Current Division
* Two simple practical analysis methods:
  Intuitive Method: Circuit Reduction
  Delta and Wye Connection

## Slide 4: Voltage Division
When do we apply voltage division?
Two conditions must be met:
All the resistors being used in the formula have the same currents.
AND
The voltage being divided is applied across all the resistors used in the division formula.
Simple circuit with two resistors in series

## Slide 5: Voltage Division
When do we apply voltage division?
Two conditions must be met:
All the resistors being used in the formula have the same currents.
AND
The voltage being divided is applied across all the resistors used in the division formula.
Simple circuit with two resistors in series
The voltage across a given resistor is equal to that resistor divided by the total of series-connected resistors multiplied by the applied voltage.

## Slide 6: Voltage Division
Assuming the following current direction and voltage polarities,
Applying KVL to the circuit below,
Simple circuit with two resistors in series
Apply Ohm’s law:

## Slide 7: Voltage Division
Solving for i yields,
Therefore, vR1 and vR2 are given by,
Simple circuit with two resistors in series

## Slide 8: Invalid Examples of Voltage Division

## Slide 9: Invalid Examples of Voltage Division

## Slide 10: Invalid Examples of Voltage Division

## Slide 11: Voltage Division Formula
In series-connected resistors, the voltage across a given resistor is equal to that resistor divided by the total of series-connected resistors multiplied by the total voltage across the total of series-connected resistors.
Simple circuit with two resistors in series

## Slide 12: Example
For the circuit given, find the voltages across the resistors by using the voltage division formula.
Values:
Circuit with three resistors in series
Variable | Default | Unit
Vs | 18 | V
R1 | 5 | Ω
R2 | 10 | Ω
R3 | 15 | Ω

## Slide 13: Example
Standard Solution – Using KVL in a Single-Loop
Assume the direction of the current and voltage polarities shown, because the current in each resistor is the same then,
Applying KVL to the loop yields,
Solving for i yields,
Assigning current direction and voltage polarities

## Slide 14: Example
Therefore, the voltages across the resistors are given by,
Assigning current direction and voltage polarities

## Slide 15: Example
Short Cut Solution – Direct application of voltage division formula:
Check:

## Slide 16: Example
Use voltage division to find the voltage across each resistor in the circuit.
Values:
Single-Loop circuit
Variable | Default | Unit
Vs | 18 | V
R1 | 25 | kΩ
R2 | 5 | kΩ
R3 | 10 | kΩ
R4 | 10 | kΩ

## Slide 17: Example
Solution:
The circuit can be redrawn as an equivalent circuit with three series resistors,
Applying the voltage division formula,
Equivalent circuit with assigned current and voltages

## Slide 18: Example
Because R3 and R4 are in parallel,
Equivalent circuit with assigned current and voltages

## Slide 19: Design Example
Consider the circuit given, select a value for the load resistor, RL, so that its voltage, vL, becomes 0.5VS =0.5x10=5V.
Values:
Circuit with load resistance
Variable | Default | Unit
VS | 10 | V
R1 | 5 | Ω
R2 | 10 | Ω
R3 | 20 | Ω

## Slide 20: Example
Solution:
To solve for vL, resistors R3 and RL are combined in parallel,
Apply the voltage division formula as follows, and substitute Req,
Equivalent circuit

## Slide 21: Example
Solution:
Set vL = 0.5VS, and solve for RL,
Equivalent circuit

## Slide 22: Current Division
To apply current division make sure that the resistors being used all have the same voltage across.
Current division gives you a simple method to find the current in single node-pair circuits.
Two resistors in parallel

## Slide 23: Current Division
Current division is not as simple as voltage division, to make the equations for current division simpler, resistance is expressed in terms of its conductance values.
Consider the circuit below,
Two resistors in parallel
is
iR1
iR2
What fraction of is flows in each resistor?

## Slide 24: Current Division
Current division is not as simple as voltage division, to make the equations for current division simpler, resistance is expressed in terms of its conductance values.
Consider the circuit below,
Two resistors in parallel
What fraction of is flows in each resistor?
Check: is=iR1+iR2

## Slide 25: Current Division
We assign current directions as shown, because the voltage across each resistor in the parallel-connected resistors is v,
Applying KCL at the upper node connects all the resistors to yield
Current directions assigned

## Slide 26: Current Division
Substitute for v, and solve for iR1 and iR2, respectively,
Current directions assigned

## Slide 27: Current Division
Direct application of current division formula:
Check: is=iR1+iR2

## Slide 28: Current Division
The equations of iR1 and iR2 consist of dividing the reciprocals of resistors.
Therefore, some test tools use the conductance, G, to express the current division formulas as shown,
Where,
Current directions assigned

## Slide 29: Example
Use the current division method to find the current in each resistor in the circuit given.
Values:
Circuit with load resistance
Variable | Default | Unit
IS | 12 | A
R1 | 10 | Ω
R2 | 20 | Ω
R3 | 14 | Ω
R4 | 16 | Ω

## Slide 30: Example
Solution:
First, combine R3 and R4 in series,
Applying the current division formula,
Equivalent circuit

## Slide 31: Example
Equivalent circuit
Check: 6.5+3.3+2.2= 12 A = Is
?

## Slide 32: Example
Where,
The currents in R3 and R4 are equal to the current passing through the resistor Req as follows,
Equivalent circuit

## Slide 33: Design Example
Consider the circuit given, select the value for the load resistor, RL, so that its current, iL, becomes IS =0.5IS (the load current is at 50% of Is).
Values:
Circuit with load resistance
Variable | Default | Unit
IS | 12 | A
R1 | 20 | kΩ
R2 | 20 | kΩ
R3 | 8 | kΩ

## Slide 34: Example
Solution:
First, combine R1 and R2 in parallel as shown,
Equivalent circuit

## Slide 35: Example
Solution:
Also combine the resistors R3 and RL in series as shown below, now we can apply the current division rule as follows,
Set iL = 0.5IS, and solve for RL
Equivalent circuit

## Slide 36: Example
Find the voltage across the load resistor vL for the circuit using current division.
Circuit with load resistance
Variable | Default | Unit
IS | 4 | A
R1 | 5 | Ω
R2 | 10 | Ω
R3 | 10 | Ω
R4 | 20 | Ω
RL | 10 | Ω
β | 2 | -
Values:

## Slide 37: Example
Find the voltage across the load resistor vL for the circuit using current division.
Circuit with load resistance
Variable | Default | Unit
IS | 4 | A
R1 | 5 | Ω
R2 | 10 | Ω
R3 | 10 | Ω
R4 | 20 | Ω
RL | 10 | Ω
β | 2 | -
Values:
i=?

## Slide 38: Example
Find the voltage across the load resistor vL for the circuit using current division.
Circuit with load resistance
Variable | Default | Unit
IS | 4 | A
R1 | 5 | Ω
R2 | 10 | Ω
R3 | 10 | Ω
R4 | 20 | Ω
RL | 10 | Ω
β | 2 | -
Values:
i=?

## Slide 39: Example
Solution:
The current passing through resistor R2,
Using the current division formula,
the voltage across the load resistor, vL,
Circuit with load resistance

## Slide 40: 1752
Benjamin Franklin conducts famous ‘kite experiment’ to study electricity
Benjamin Franklin, one of the founding fathers, won great fame for his study of electricity. He developed the theory of ‘positive’ and ‘negative’ electricity, showed the effect of pointed bodies in drawing off electricity, studied the identity of lightning and electricity, and recognized the potential of using iron rods to protect buildings. His famous kite and key experiment drew down electricity from the clouds and charged a Leyden jar.
Benjamin Franklin – American Scientist and Inventor
(1706 - 1790)

## Slide 41: Intuitive Method: Circuit Reduction
Reduce the number of components to an equivalent simplified circuit.
The final number of nodes and loops are significantly reduced.
Elements with currents and voltages of interest are left alone as given in the original circuit.
Does not follow a specific procedure, but rather depends on experience.

## Slide 42: Example
Use the circuit reduction method to find the current ix shown in the circuit.
Values:
Resistive circuit
Variable | Default | Unit
V | 18 | V
R1 | 5 | kΩ
R2 | 3 | kΩ
R3 | 8 | kΩ
R4 | 4 | kΩ
R5 | 7 | kΩ
R6 | 11 | kΩ

## Slide 43: Example
Solution:
To find the current ix, find the equivalent resistance as seen from terminals “a” and “b” as shown,
Circuit with load resistance

## Slide 44: Solution (con’d)
The circuit below shows the equivalent circuit after replacing all the resistors with one resistor Req,
Thus,
Circuit with load resistance

## Slide 45: Example
Use the circuit reduction method to find the current ix shown in the circuit.
Values:
Resistive circuit
Variable | Default | Unit
I | 8 | A
R1 | 10 | Ω
R2 | 10 | Ω
R3 | 20 | Ω
R4 | 20 | Ω
R5 | 15 | Ω
R6 | 25 | Ω

## Slide 46: Example
Solution:
Because the current of interest is in the middle of the circuit, you combine the resistors in such a way that the R2 branch always remains by itself in the reduced circuit.
By combining R3 and R4 in parallel and R5 and R6 in series,
Reducing the circuit

## Slide 47: Example (Solution-cont’d)
Then you combine R2 in series with (R3//R4).
Then, R1 is combined in parallel with (R5+R6) as shown
Reducing the circuit
Reducing the circuit

## Slide 48: Example (Solution-cont’d)
Now you apply current division to solve for ix to yield,
Reducing the circuit

## Slide 49: Example - Combining Resistors
What is the equivalent resistance seen between terminals “a” and “b?
Req ?

## Slide 50: Example - Combining Resistors
What is the equivalent resistance seen between terminals “a” and “b?
Req ?
None of the resistors are in series or in parallel !!!

## Slide 51: Example - Combining Resistors
One way to find the resistance between “a” and “b” is to set-up an experiment in the lab and apply a battery across terminals “a” and “b”:
None of the resistors are in series or in parallel !!!
Step 1: Measure I
Step 2: Since you know V, then carry out Ohm’s Law

## Slide 52: Delta and Wye Connections
In some resistor circuits, none of the resistors can be combined either in series or in parallel.
Wye and delta circuit interconnections are the most common configurations where resistors cannot be simplified by simple series or parallel.
Delta (△)
Wye (Y)

## Slide 53: Delta and Wye Connections
Other configuration of Wye and delta circuit interconnections:
Delta (△)
Wye (Y)

## Slide 54: Delta and Wye Connection
In these two cases, we use a method known as the delta-to-wye (∆ Y) and wye-to-delta (Y ∆) transformations.
Circuit Transformation

## Slide 55: Delta and Wye Transformation
Wye and delta circuit interconnections can be transformed from one configuration to the other by properly adjusting their resistor values.
To transform the ∆ configuration to Y configuration, you use the following relations:
∆→Y and Y→∆ transformation

## Slide 56: Delta and Wye Connection
∆→Y and Y→∆ transformation
If all resistors in a given structure are equal as shown, then the transformation equations are simplified as follows:

## Slide 57: The most Common Connection – The Bridge Circuit
For example, for the circuit shown, we are interested in finding the total equivalent resistance Req between terminals a and b.
No possible combination of resistors is allowed

## Slide 58: Delta Connection
Notice that there are two possible ways to from Delta connections as shown.
1) Delta 1: Resistors R1, R2, and R5
2) Delta 2: Resistors R3, R4, and R5

## Slide 59: Delta Connection
Notice that there are two possible ways to from Wye connections as shown.
1) Wye 1: Resistors R2, R4, and R5
2) Wye 2: Resistors R1, R3, and R5

## Slide 60: Example
Consider the problem of finding Req for the circuit shown:

## Slide 61: Example (solution)
Resistive circuit
Solution (A) – Use the upper ∆ to Y transformation):
Consider transforming the ∆ configuration formed by resistors R1, R2, and R5 as shown:

## Slide 62: Example (solution-cont’d)
From the ∆-to-Y transformation equations come the following equations:

## Slide 63: Example (solution-cont’d)
From the ∆-to-Y transformation equations come the following equations:

## Slide 64
Resistive circuit
Solution (B) Use the lower ∆ to Y transformation):
Consider transforming the ∆ configuration formed by resistors R3, R4, and R5 as shown;
Example (solution-cont’d)

## Slide 65
Resistive circuit
Solution (C) - Use the right Y to ∆ transformation):
Consider transforming the Y configuration formed by resistors R2, R4, and R5 as shown:
Example 3 (solution-cont’d)

## Slide 66
Resistive circuit
Solution (D) – Use the left Y to ∆ transformation):
Consider transforming the Y configuration formed by resistors R1, R3, and R5 as shown:
Example (solution-cont’d)

## Slide 68
In another words find i first then find

## Slide 69
In another words find i first then find
Dr. Batarseh’s Pearson eText – Copy Rights Protected

## Slide 71
Redrawn as follows:

## Slide 72
Next, combine R1' and R5 in parallel and R3' and R4 also in parallel as shown:
Finally, is obtained by combining the two resistors of Figure 3.58(d) in series to yield

## Slide 73
The total power defined by the voltage source vs is given by,

## Slide 75
From the ∆-to-Y transformation equations come the following equations:

## Slide 77
Finally, Req is obtained by combining the two resistors in series to yield,
The total power defined by the voltage source vs is given by,

## Slide 80: Example
Find the equivalent resistance, Req, seen between terminals “a” and “b”.
Combination of resistors
Variable | Values | Unit
R1 | 7.5 | kΩ
R2 | 4 | kΩ
R3 | 2 | kΩ
R4 | 6 | kΩ
R5 | 2 | kΩ
R6 | 1 | kΩ
R7 | 3 | kΩ

## Slide 81: Example (Solution)
Solution:
The circuit can be simplified as shown, where,
Parallel combination

## Slide 82: Example
The circuit can be simplified as shown, where,
The circuit can be simplified as shown, where,
Series combination
Parallel combination

## Slide 83: Example
The circuit can be simplified as shown, where,
The circuit can be simplified as shown, where,
Series combination
Parallel combination

## Slide 84: Example
The circuit can be simplified as shown, where,
Series combination

## Slide 85: Example 6
For the circuit, given the values of Vo and all resistors, find:
The equivalent resistance, Req, seen between terminals “a” and “b”.
The current leaving the voltage source, i.
Resistive circuit
Variable | Values | Unit
Vo | 10 | V
R1 | 4 | kΩ
R2 | 1 | kΩ
R3 | 3 | kΩ
R4 | 4 | kΩ
R5 | 6 | kΩ
R6 | 6 | kΩ
R7 | 3 | kΩ
R8 | 5 | kΩ
R9 | 4 | kΩ

## Slide 86: Example
For the circuit, given the values of Vo and all resistors, find:
The equivalent resistance Req seen between terminals “a” and “b”.
The current leaving the voltage source, i.
Resistive circuit
Variable | Values | Unit
Vo | 10 | V
R1 | 4 | kΩ
R2 | 1 | kΩ
R3 | 3 | kΩ
R4 | 4 | kΩ
R5 | 6 | kΩ
R6 | 6 | kΩ
R7 | 3 | kΩ
R8 | 5 | kΩ
R9 | 4 | kΩ
Req

## Slide 87: Example (Solution)
Solution:
a) By inspection, R7, R8 and R9 are in series as well as R5 and R6 and R2 and R3. The circuit in Figure P 2.5(a) can be simplified to the one shown,
Equivalent circuit

## Slide 88: Example 6 (Solution)
Moreover, the circuit can be simplified to the one shown,
Equivalent circuit

## Slide 89: Example (Solution)
Moreover, the circuit can be simplified to the one shown,
b) Using Ohm’s law, we obtain,
Equivalent circuit
The total resistance seen by the voltage source Vo is 5.5 kΩ

## Slide 90: Example
Consider the circuit with all the parameters are given. Find the current i.
Resistive circuit
Variable | Values | Unit
Vo | 10 | V
R1 | 8 | Ω
R2 | 4 | Ω
R3 | 9 | Ω
R4 | 4 | Ω
R5 | 10 | Ω
R6 | 3 | Ω
R7 | 7 | Ω

## Slide 91: Example (Solution)
Solution:
We start by reducing the circuit as seen,
Equivalent circuit – Single Loop
Apply Ohm’s law,

## Slide 92: Example (Solution)
What if we ask for voltages ?
=-0.61x4.5= -2.8 V

## Slide 93: Example (Solution)
What if we ask for voltage v?
Apply voltage division:
=

## Slide 94
Check your answer
Let us assign as shown above. Then we must have
Notce, the current is given by,
So, we have
Now let us check your answer

## Slide 95: Example (Solution)
What if we ask for voltage v?
Apply voltage division:
=