## Slide 1: EEL 3004 Linear Circuits I Lecture #7 Simple Circuit Analysis Voltage and Current Source Transformation

## Slide 2: Exam I: Closed Book/notes Enable your camera to show your workspace
Wednesday, Feb. 24 | Exam I: 10:30 – 11:45 AM | Lectures 1-10 (Chs. 1-4(part)
REMINDER

## Slide 3: Simple Circuit Analysis Techniques
Chapter Three
Chapter Outline
Introduction
3.1 Analysis of Single-Loop Circuits
3.2 Analysis of Single-Node-Pair Circuits
3.3 Voltage and Current Division
3.4 Intuitive Analysis Method: Circuit Reduction
3.5 Voltage and Current Source Transformation

## Slide 4: Lecture Objectives
The lecture today will focus on:
Ø Know how to convert voltage source to current source and vice versa.
Ø Be able to use voltage source to current source to obtain single-­‐node-­‐pair circuits
Ø Be able to use current source to voltage source to obtain single-­‐loop circuits
Ø Solving Examples using Source Transformation

## Slide 5: Source Transformation
Vs
R
a
b
Is
R
a
b
Between node (a) and (b):
Voltage source Vs in series with resistor R can be replaced by a current source Is in parallel with R and vice versa.
Condition:

## Slide 6: Proof:
VL =
Vs
RL + R
[RL ]
Vs
R
a
b
VL
RL
IL
Is
R
a
b
VL
RL
IL
IL =
Vs
R + RL
VL = [Is ]⎢
⎡ R RL ⎤
⎣ R + RL ⎦
⎥
IL = [Is ]⎢ R + R ⎥
⎡ R ⎤
L ⎦
⎣
Concept of equivalent circuits
The (i-v) characteristic between (a) and (b) are identical
IS =
Vs R
If and only if

## Slide 7
Example
Connect resistor RL between (a) and (b) in the two circuits
Find :
VL = ?
iL = ?
For:
RL = 7Ω
3Ω
a
iL
b
10V
RL = 7Ω
vL
10
A
3
a
b
3Ω L
iL
RL = 7Ω
v

## Slide 8
10V
3Ω
a
iL
b
RL = 7Ω
vL
10
A
3
b
3Ω
a
iL
R = 7Ω
L
v
L
VL = (10)
7
3 + 7
V = 7V
L
iL =
10
3 + 7
iL = 1A
iL = 1A
VL = 7V
For the resistive load, the two circuits are equivalent!

## Slide 9
Vs
R
a
b
VL
RL
IL
Is
R
a
b
VL
RL
IL
Is =
Vs R
Important Note:
If the polarity of the voltage source is reversed, the direction of the current source must also be reversed as shown.

## Slide 10
2mA
2.7kΩ
1kΩ
2.3kΩ
io
0.6mA
Example – Use source transformation to find io
Use source transformation to find :
io = ?

## Slide 11
2.3kΩ
2mA
2.7kΩ
1kΩ
io
0.6mA
a
•
•
c
•
•
c
b
2.7kΩ a 2.3kΩ
•
0.6V
io
5.4V
1kΩ
•
b
•
c
Solution:
KVL:
−0.6 − io (1 + 2.3 + 2.7)k − 5.4 = 0
io = −1mA

## Slide 12
Example
Use the source transformation method to solve for all currents in the circuit.
Variable | Values | Unit
I | 8 | A
R1 | 5 | Ω
R2 | 15 | Ω
R3 | 10 | Ω

## Slide 13: Solution
Let us transform the current source I to voltage source:
V=IR3
Equivalent Single-­‐ Loop Circuit

## Slide 14: Solution
KVL:
+ IR3 = 0
R1ia + R2ia + R3ia
−2.7 A
i =
a
Assign current ia as shown:

## Slide 15: Solution
The current in R1 and R2 is equal to ia
KCL at node va:
iR = I + ia
3
= 8 + (−2.7)= 5.3 A
Note: After using the source transformation, we can go back to the original circuit to find other values of current and voltage.

## Slide 16
Use the current-­‐to-­‐voltage transformation method to solve for all currents in the circuit.
Example
Variable | Values | Unit
V | 10 | V
I | 8 | A
R1 | 5 | Ω
R2 | 15 | Ω
R3 | 25 | Ω

## Slide 17
KVL:
= 9.4 Ω
= R2 // R3
Req
− V + R1ia + Req ia − IReq = 0
= 5.9 A
R1 + Req
IReq + V
ia =
Solution

## Slide 18
KCL at node va:
ia = I + iR
eq
= −2.1 A
iR = ia − I
eq
Next, obtain the individual currents in R2 and R3 by using Ohm’s
= −19.6 V
Req
= iR
vR = vR = vR
2 3 eq
eq
= −1.3 A
R2
R2
The current in R1 is equal to ia
v v
i =
R2
= −0.78 A
R3
i =
R3
R3
Solution

## Slide 19
Example
Use the source transformation method to solve for all currents in the circuit.
For:
Variable | Values | Unit
V | 10 | V
I1 | 8 | A
I2 | 8 | A
R1 | 5 | Ω
R2 | 3 | Ω
R3 | 6 | Ω

## Slide 20
KVL:
− V + R1ia + R2ia − I1 R2 + R3ia + I 2 R3 = 0
= −1 A
R + R + R
i = V + R2 I1 − R3 I 2
a
3
2
1

## Slide 21
Example
By using source transformation, solve for vx and ix.
For:
Variable | Values | Unit
V | 12 | V
I | 8 | A
R1 | 4 | Ω
R2 | 3 | Ω

## Slide 22
KCL: to the upper node
vx
+ + I = 0
R1 R1 R2
− V + vx
(V − R I )
= −8.6 V
R1 + R2
R2
v =
x
1
= 2.9 A
R2
= − vx
i
x

## Slide 23
Example
Use source transformation to find vL:

## Slide 24
Solution:

## Slide 25
KVL:
-10 + 6iL - 18 + 8iL + 2iL = 0
16iL = 28
iL = 1.75A
vL = 1.75(8) = 14V

## Slide 26
Example: Use Source Transformation to find Vo
Solution:
Identify series V+R or Parallel I+R:
Since we need Vo, we start at the other end to keep Vo as is.

## Slide 27
Solution:

## Slide 28
Solution:

## Slide 29
3mA
1kΩ
2kΩ
2kΩ
4mA
Vo
−
+
a
•
•
b
1kΩ
2kΩ
2kΩ
4mA
Vo
−
+
a
•
•
b
3V
c
•

## Slide 30
c
•
2kΩ
4mA
Vo
−
+
•
b
3kΩ
1mA
4mA 1.2kΩ
Vo
−
+
•
b
c
•
5mA
V = (5mA)(1.2kΩ)
o
Vo = 6V
3kΩ
2kΩ
Vo
−
+
•
b
3V
c
•
4mA

## Slide 31
Example of Source Transformation – Find vx

## Slide 32
Apply KVL around the left loop:
Recall before that we can find

## Slide 33
Apply KVL:

## Slide 34
Apply KVL:
Apply KVL:
Apply KVL:

## Slide 35
Check
Apply KVL to the outer loop:

## Slide 36
Use source transformation to find :
The voltage across the 8 Ohms resistor. The power related to the current source
The power related to the 120V source
Example

## Slide 37
120V
60V
36A
5Ω
6Ω
8Ω
a
20Ω
1.6Ω
v
i
8
b
Approach:
Find the current through the 8 Ohm resistor,
Find the voltage across the current source Find the current through the 120V source.
i
20
Solution:

## Slide 38
b
12A
6Ω
1.6Ω
8Ω
36A
a
6A
20Ω
5Ω
Use Source Transformation to get
120V
5Ω
6Ω
36A
a
20Ω
1.6Ω
8Ω
b
60V

## Slide 39
Combine the resistors in parallel and the current sources in parallel to get:

## Slide 40
KVL:
120 + 20(i20 ) − V = 0
i20 = −3.12 A
120 + 20(i20 ) − 57.6 = 0

## Slide 41: Example
By using source transformaHon, solve for vx and ix.
Variable | Values | Unit
V1 | 20 | V
V2 | 12 | V
I | 8 | A
R1 | 5 | Ω
R2 | 10 | Ω
R3 | 15 | Ω

## Slide 42
s

## Slide 44
What about ix?

## Slide 45
Notice, ix has been removed.
We must work backward to solve for ix in the original circuit.
Let us assign iy as shown

## Slide 47
Problem 1:
Source Transformation
2mA
2kΩ
6kΩ
3kΩ
6V
3kΩ
a
b
b
c
c
c
c
Io
2kΩ
6kΩ
3kΩ
3kΩ
c
b
c
a
6V
6V
Io
2kΩ
6kΩ
6kΩ
c
a
6V
6V
Io
2kΩ
6kΩ
6kΩ
c
a
1mA
1mA
Io
2kΩ
3kΩ
c
a
Io
2mA
Io = 2m
3k
3k + 2k
I = 1.2mA
o

## Slide 48
Problem (2) Source Transformation
6V
2kΩ
2kΩ
2kΩ
2kΩ
4mA
Vo
−
+
a
•
•
b
3mA
2kΩ
2kΩ
2kΩ
2kΩ
4mA
Vo
−
+
a
•
•
b

## Slide 49
3mA
1kΩ
2kΩ
2kΩ
4mA
Vo
−
+
a
•
•
b
1kΩ
2kΩ
2kΩ
4mA
Vo
−
+
a
•
•
b
3V
c
•

## Slide 50
c
•
2kΩ
4mA
Vo
−
+
•
b
3kΩ
1mA
4mA 1.2kΩ
Vo
−
+
•
b
c
•
5mA
V = (5mA)(1.2kΩ)
o
Vo = 6V
3kΩ
2kΩ
Vo
−
+
•
b
3V
c
•
4mA

## Slide 51
Problem (3)-­‐ Source transformation
6V
3kΩ
5V
2kΩ
−
2kΩ
2mA 1kΩ
1kΩ
Vo
+
•
a
•
b
c
•
•
b
3kΩ
2mA
2kΩ
2.5mA
2kΩ
2mA 1kΩ
1kΩ
Vo
a
• +
−
b
•
c
•
•
b

## Slide 52
0.75kΩ
1.5mA
1kΩ
1kΩ
Vo
a
• +
−
b
•
•
c
•
b
1kΩ
1kΩ
Vo
a
• +
−
•
b
c
•
•
b
0.75kΩ
1.125V
Vo = (1.125)
1k
2.75k
Vo = 0.41V

## Slide 53
12V
12kΩ
3kΩ
6kΩ
Io
3kΩ
6kΩ
6kΩ
2mA
Problem (4) Source Transformation
Find the current
Io = ?

## Slide 54
Solution:
12V
12kΩ
6kΩ
Io
a
b
c
3kΩ
6kΩ
6kΩ
d
e
e
6V
3kΩ
12V
12kΩ
6kΩ
Io
a
b
12kΩ
6kΩ
e
e
0.5mA
12V
12kΩ
6kΩ
I
o
a
b
12kΩ
6kΩ
e
e
6V
b
12V
12kΩ
3kΩ
6kΩ
Io
a
b
•
e •
c
d
3kΩ
6kΩ
6kΩ
2mA
d
e
e
•
•
•
•

## Slide 55
12kΩ
Io
b
12kΩ
e
b
6kΩ
0.5mA
6kΩ
2mA
Io
6kΩ
e
3kΩ
1.5mA
Io = −1.5m 3k + 6k
3k
Io = −0.5mA

## Slide 56
Problem (5)
1A
6Ω
io
1.5Ω
17Ω
34V
5Ω
6Ω
2A
Use source transformation to find :
io = ?

## Slide 57
Problem (6)
1A
6Ω
io
a
•
•
d
•
•
b
c
1.5Ω
17Ω
34V
5Ω
6Ω
2A
•
d
6Ω
io
•
d
•
c
•
a
•
b
1.5Ω
17Ω
34V
+
−
•
d
12V
6Ω
5V
5Ω

## Slide 58
io
1.5Ω
1A
17Ω
2A
17Ω
•
•
d
c
1A
8.5Ω
1.5Ω
io
•
•
d
c
io = −1 = −0.85A
8.5 + 1.5
8.5
io
•
d
c
•
1.5Ω
17Ω
34V
17Ω
17V

## Slide 59
100V
20kΩ
3kΩ
80kΩ
1kΩ
12mA
60kΩ
5kΩ
10kΩ
io
Problem ( 7)
Find
io = ?

## Slide 60
100V
20kΩ
3kΩ
80kΩ
1kΩ
12mA
60kΩ
5kΩ
10kΩ
io
a
•
•
•
•
d
b
•
•
d
b
c
3kΩ
80kΩ
1kΩ
12mA
60kΩ
5kΩ
10kΩ
io
a
•
•
•
•
d
b
•
•
d
b
c
20kΩ
5mA

## Slide 61
3kΩ
16kΩ
1kΩ
12mA
60kΩ
5kΩ
10kΩ
io
a
•
•
c
•
•
d
b
•
•
d
b
5mA
3kΩ
16kΩ
1kΩ
12mA
60kΩ
5kΩ
10kΩ
io
a
•
•
c
•
•
d
b
•
•
d
b
80V

## Slide 62: 20kΩ
12mA
60kΩ
5kΩ
10kΩ
io
•
•
d
b
•
•
b
80V
12mA
60kΩ
5kΩ
10kΩ
io
•
•
d
b
•
•
b
20kΩ
4mA

## Slide 63
•
120V
15kΩ
5kΩ
10kΩ
io
•
b
•
d
io =
120
(15 + 5 + 10)k
i = 4mA
o
 |  |  | 5kΩ |  | 
 |  |  |  | io | 
 | 8mA |  | 15kΩ |  | 10kΩ
b
d
b

## Slide 64
Problem (8)
520V
1A
16Ω
260Ω
40Ω
6Ω
4Ω
250Ω
+
−
vo
520V
vo =?

## Slide 65
1A
16Ω
Note !!
RL
a
•
b
The load voltage and the load current are the same!
1A
RL
a
•
b
RL
a
•
•
b
520V
260Ω
RL
a
•
b
520V

## Slide 66
Problem (9)
520V
1A
16Ω
260Ω
40Ω
6Ω
4Ω
250Ω
c
•
+
d
−
vo
a
•
•
b
e
520V
1A
40Ω
6Ω
4Ω
250Ω
c
•
+
d
−
vo
a
•
•
b
e

## Slide 67
6Ω
4Ω
250Ω
c
•
+
d
−
vo
a
•
•
e
b
40V
40Ω
vo =
( 520 − 40 )( 250 )
(40 + 4 + 6 + 250)
vo = 400V
520V