## Slide 1: EEL 3004 Linear Circuits I Lecture #14 First Order RC Circuits - Natural responses

## Slide 2: Reading Materials
Chapter 6 – Transient Response for RL and RC Circuits
Only the following sections:
6.1 The First Order Circuits
6.3 Natural Response of RC Circuits
6.4 Natural Response of RL Circuits

## Slide 3: Lecture Objectives
This lecture will focus on:
Review of RC circuits with DC sources under switching (natural response).
Natural response in RC Circuits with DC sources
Examples

## Slide 4
If the circuit consists only of direct current and voltage sources (dc), and the switch has been closed or opened for long time, then the capacitor behaves as an open circuit, and the inductor behaves as a short circuit.
RLC circuits with DC sources and NO Switching
(Steady-state)
Under DC conditions – the circuit has been undisturbed for a long time

## Slide 5
RC circuits with DC sources under switching
(Transient-state)
Assume the switch has been closed for long time, then
At time t=0, the switch is opened.
What happens to the capacitor voltage after the current source
has been removed?
This circuit will respond naturally due to its circuit values and the way they are arranged.
We call it natural response or transient response.
Our goal to find the voltages, currents and power after t > 0.

## Slide 6
RC circuits with DC sources under switching
(Transient-state)
This circuit will respond naturally due to its circuit values and the way they are arranged.
We call it natural response or transient response.
R’s and L’s In Series
Our goal to find the voltages, currents and power after t > 0.

## Slide 7
The natural response for an RC circuits are obtained when the external independent source is set to zero (removed).
For the natural responses to exist it is required that the capacitor has energy stored in it at the moment of switching.
Natural Response of RC circuits
R’s and C’s
No External source
After certain action (switching)
Determine the currents and voltages (natural responses)

## Slide 8
IMPORTANT DEFINITIONS
Natural Response of RC circuits
For t < 0, we let
For t > 0, we let
Therefore, for the capacitor:
=

## Slide 9
Finding the Natural Response of RC circuits
Find for t < 0 (Before the switching action took place)
We follow two-step process:
=
But, since we have dc sources and no switching action for long time, the capacitor voltage is constant and is equal to,
For all time t < 0
II) Find for t > 0 (After the switching action took place)
The new circuit
An ordinary 1st order DEQ with constant coefficients
is the overall time constant
is the initial capacitor value across
General solution

## Slide 10
Finding the Natural Response of RC circuits
1) When
Notice the following:
= = 0.37
This means after one time constant () the capacitor voltage drops to 37% of its initial value of
2) When
= = 0.0067
This means after five time constant () the capacitor voltage drops to 0.67% of its initial value of
The capacitor voltage drops by 63% from its original value
The capacitor voltage drops by 99.33% from its original value

## Slide 11
Typical Sketch for Natural Response of RC circuits
0.37
0.01

## Slide 12
Any given resistive-capacitive circuit without external independent DC sources that can be reduced to a parallel equivalent RThCeq circuit.
The general solution for vC(t) is given,
General Natural Response of RC circuits
is the overall time constant
is the initial capacitor value across

## Slide 13
Example
For the following RC circuit with a DC voltage source. Initially the switch has been connected to position ‘a’ for a long time. At t=0, the switch moved to position ‘b’.
Determine the voltage response for vC(t), for t≥0,
Variable | Values | Unit
Vo | 8.6 | V
R | 4.5 | kΩ
Ro1 | 8 | kΩ
Ro2 | 16 | kΩ
C | 2.1 | mF

## Slide 14
For t < 0 the capacitor is fully charged. Hence at t=0- we have,
Step 1: Find vc for t < 0 (Long time when the switch was in position a):
= =5.7 V
Therefor,

## Slide 15
For t > 0,
Step 2: Find vc for t > 0 (after the switch is moved to position b):
The general solution for vC(t) is given by,
= =5.7 V
F = 9.5 seconds
Note:
When R in Ohms and C in Farads gives time in seconds
Volts

## Slide 16
Example
For the following RC circuit with a DC voltage source. Initially the switch has been connected to position ‘a’ for a long time. At t=0, the switch moved to position ‘b’. Determine:
The voltage response for vC(t), for t≥0,
The current iR1(t) for t>0,
What is the voltage across the capacitor at t=3 s, 15 s and 30s.
Variable | Values | Unit
Io | 2 | mA
R1 | 4.5 | kΩ
R2 | 2.4 | kΩ
Ro1 | 8 | kΩ
Ro2 | 16 | kΩ
Ro3 | 24 | kΩ
C | 2.1 | mF

## Slide 17
For t < 0 the capacitor is fully charged and acts like an open circuit.
Hence at t=0- we have,
= = 8 V
Therefor,

## Slide 18
For t > 0,
Calculating ,
=
=
= 3.29 seconds
(a) Substituting these values in the general expression for for t>0,
Volts

## Slide 19
(b) The current across the resistor can be calculated as,
mA
Similarly,
mA

## Slide 20
The current across the resistor can be calculated as,
mA
Similarly,
mA
Check:
mA
C)
= (
=5.04 mA
But

## Slide 21
c) What is the voltage across the capacitor at t=1 s, 3.3 s, 15 s and 30s.
5.93 V
At t=1 s
At t=3.3 s (
V
At t=15 s (
V
V
At t=30 s