## Slide 1: EEL 3004 Linear Circuits I Lecture #14 First Order RC Circuits - Natural responses

## Slide 2: Reading Materials
Chapter 6 – Transient Response for RL and RC Circuits
Only the following sections:
6.1 The First Order Circuits
6.3 Natural Response of RC Circuits
6.4 Natural Response of RL Circuits

## Slide 3: Lecture Objectives
This lecture will focus on:
Review of RC circuits with DC sources under switching (natural response).
Natural response in RC Circuits with DC sources
Examples

## Slide 4
If the circuit consists only of direct current and voltage sources (dc), and the switch has been closed or opened for long time, then the capacitor behaves as an open circuit, and the inductor behaves as a short circuit.
RLC circuits with DC sources and NO Switching
(Steady-state)
Under DC conditions – the circuit has been undisturbed for a long time

## Slide 5
RC circuits with DC sources under switching
(Transient-state)
Assume the switch has been closed for long time, then
At time t=0, the switch is opened.
What happens to the capacitor voltage after the current source
has been removed?
This circuit will respond naturally due to its circuit values and the way they are arranged.
We call it natural response or transient response.
Our goal to find the voltages, currents and power after t > 0.

## Slide 6
RC circuits with DC sources under switching
(Transient-state)
This circuit will respond naturally due to its circuit values and the way they are arranged.
We call it natural response or transient response.
R’s and L’s In Series
Our goal to find the voltages, currents and power after t > 0.

## Slide 7
The natural response for an RC circuits are obtained when the external independent source is set to zero (removed).
For the natural responses to exist it is required that the capacitor has energy stored in it at the moment of switching.
Natural Response of RC circuits
R’s and C’s
No External source
After certain action (switching)
Determine the currents and voltages (natural responses)

## Slide 8
IMPORTANT DEFINITIONS
Natural Response of RC circuits
For t < 0, we let
For t > 0, we let
Therefore, for the capacitor:
=

## Slide 9
Finding the Natural Response of RC circuits
Find for t < 0 (Before the switching action took place)
We follow two-step process:
=
But, since we have dc sources and no switching action for long time, the capacitor voltage is constant and is equal to,
For all time t < 0
II) Find for t > 0 (After the switching action took place)
The new circuit
An ordinary 1st order DEQ with constant coefficients
is the overall time constant
is the initial capacitor value across
General solution

## Slide 10
Finding the Natural Response of RC circuits
1) When
Notice the following:
= = 0.37
This means after one time constant () the capacitor voltage drops to 37% of its initial value of
2) When
= = 0.0067
This means after five time constant () the capacitor voltage drops to 0.67% of its initial value of
The capacitor voltage drops by 63% from its original value
The capacitor voltage drops by 99.33% from its original value

## Slide 11
Typical Sketch for Natural Response of RC circuits
0.37
0.01

## Slide 12
Assume the switch was closed for a long time.
Switch that is opened at t=0 to remove the applied current source.
Find the natural response (voltage vc) after the switch has been opened.
Natural Response of RC circuits
t > 0
No voltage or current sources

## Slide 13
Since we have DC current, therefore, the capacitor behaves like an open circuit prior to opening the switch.
Since the voltage on the capacitor cannot change instantaneously,
Finding the Natural Response of RC circuits
I) Find for t < 0 (Long time when the switch was closed):

## Slide 14
The equivalent circuit for t > 0.
Applying KVL around the loop.
Natural Response of RC circuits
An ordinary first-order differential equation (DEQ) with constant coefficients
II) Find vC(t) for t > 0 (The time after the switch is opened):

## Slide 15
Solve first order DEQ:
Natural Response of RC circuits
Integrate the above equation from t=0 to t:
Re-arrange the above equation,

## Slide 16
The final expression is given by,
Where,
Natural Response of RC circuits
Time constant
Capacitor initial value

## Slide 17
The final expression is given by,
Natural Response of RC circuits
At t=5 the capacitor voltage becomes practically zero.

## Slide 18
The induced current in the resistor, is the same as the induced current in the capacitor,
Natural Response of RC circuits

## Slide 19
Instantaneous power in the resistor,
Instantaneous energy dissipated in the resistor,
Natural Response of RC circuits

## Slide 20
At t=0, the energy dissipated in the resistor starts at zero value, and as t∞ it reaches,
Which is the amount of energy that was initially stored in the capacitor at t=0.
Natural Response of RC circuits

## Slide 21
Any given resistive-capacitive circuit without external independent DC sources that can be reduced to a parallel equivalent RThCeq circuit.
The general solution for vC(t) is given,
General Natural Response of RC circuits
is the overall time constant
is the initial capacitor value across

## Slide 22
Example
For the following RC circuit with a DC voltage source. Initially the switch has been connected to position ‘a’ for a long time. At t=0, the switch moved to position ‘b’. Determine:
The voltage response for vC(t), for t≥0,
The current iR(t) for t>0,
The total energy dissipated in R at t=, 5, and ∞.
Variable | Values | Unit
Vo | 8.6 | V
R | 4.5 | kΩ
Ro1 | 8 | kΩ
Ro2 | 16 | kΩ
C | 2.1 | mF

## Slide 23
The key is to find the for after the switching action , i.e. for .
Once we solve for then all the currents, voltages, power and energy can be expressed in terms of .
The inductor current is known as state variable
Solution A – Use the General Formula – short cut
The solution approach:
Let us use two possible solution methods:
Solution B – Use differential Equation (DEQ) approach directly – finding the integral

## Slide 24
For t < 0 the capacitor is fully charged. Hence at t=0- we have,
Step 1: Find vc for t < 0 (Long time when the switch was in position a):
= =5.7 V
Therefor,
Solution A – Use the General Formula – short cut

## Slide 25
For t > 0,
Applying KCL to the top node yields,
Substituting for iC and iR in terms of vC(t),
Rearrange as follows,
Step 2: Find vc for t > 0 (after the switch is moved to position b):

## Slide 26
Hence, the general solution for vC(t) is given by,
Calculating ,
= =5.7 V
And the initial value:

## Slide 27
Solution B – Use differential Equation (DEQ) approach directly – finding the integral
Rearrange as follows,
Write KVL equation,

## Slide 28
Integrate the above equation for all t – general solution for all t:
Where D is general constant.
Solving for vC(t),
K
We need to find K!

## Slide 29
Evaluating the above equation at t=0,
Hence, the general solution for vC(t) is given by,
Calculating ,

## Slide 30
The current across the resistor can be calculated as,

## Slide 31
The current across the resistor can be calculated as,
The total energy dissipated in R is given by,

## Slide 32
Energy dissipated at different times can be found as,
All the initial energy that was stored in C is released to R as t  ∞

## Slide 33
Example
For the following RC circuit with a DC voltage source. Initially the switch has been connected to position ‘a’ for a long time. At t=0, the switch moved to position ‘b’.
Determine the voltage response for vC(t), for t≥0,
Variable | Values | Unit
Vo | 8.6 | V
R | 4.5 | kΩ
Ro1 | 8 | kΩ
Ro2 | 16 | kΩ
C | 2.1 | mF

## Slide 34
For t < 0 the capacitor is fully charged. Hence at t=0- we have,
Step 1: Find vc for t < 0 (Long time when the switch was in position a):
= =5.7 V
Therefor,

## Slide 35
For t > 0,
Step 2: Find vc for t > 0 (after the switch is moved to position b):
The general solution for vC(t) is given by,
= =5.7 V
F = 9.5 seconds
Note:
When R in Ohms and C in Farads gives time in seconds
Volts

## Slide 36
Example
For the following RC circuit with a DC voltage source. Initially the switch has been connected to position ‘a’ for a long time. At t=0, the switch moved to position ‘b’. Determine:
The voltage response for vC(t), for t≥0,
The current iR1(t) for t>0,
What is the voltage across the capacitor at t=3 s, 15 s and 30s.
Variable | Values | Unit
Io | 2 | mA
R1 | 4.5 | kΩ
R2 | 2.4 | kΩ
Ro1 | 8 | kΩ
Ro2 | 16 | kΩ
Ro3 | 24 | kΩ
C | 2.1 | mF

## Slide 37
For t < 0 the capacitor is fully charged and acts like an open circuit.
Hence at t=0- we have,
= = 8 V
Therefor,

## Slide 38
For t > 0,
Calculating ,
=
=
= 3.29 seconds
(a) Substituting these values in the general expression for for t>0,
Volts

## Slide 39
(b) The current across the resistor can be calculated as,
mA
Similarly,
mA

## Slide 40
The current across the resistor can be calculated as,
mA
Similarly,
mA
Check:
mA
C)
= (
=5.04 mA
But

## Slide 41
c) What is the voltage across the capacitor at t=1 s, 3.3 s, 15 s and 30s.
5.93 V
At t=1 s
At t=3.3 s (
V
At t=15 s (
V
V
At t=30 s

## Slide 42
Example
In the circuit, the switch has been closed for a long time and opened at t=0. Determine:
The voltage vx(t), and current ix(t) for t ≥ 0,
Energy stored in the capacitor for t = 0,
Energy dissipated in R3 at t = ∞.
Variable | Default | Unit
Io | 4 | A
Ro | 5 | Ω
R1 | 8 | Ω
R2 | 5 | Ω
R3 | 4 | Ω
C | 1.5 | F
 | 5 | Ω

## Slide 43
For t < 0 the capacitor is fully charged. Hence at t = 0- we have,
Where,
Applying KVL around the loops,
Solving for i2 yields,

## Slide 44
The initial capacitor voltage is given by,
Solving for i2 yields,

## Slide 45
After the switch is opened for t > 0,
Next we find RTh

## Slide 46
After the switch is opened for t > 0,
+ + +
Apply KVL:
=
But we have
7x1.5=10. ms

## Slide 47
Solving for vx(t),
Where,

## Slide 48
The current ix(t) is calculated as follows,

## Slide 49
The initial energy stored in the capacitor,
The total energy dissipated in R3 is given by,

## Slide 50
For t > 0,
Therefore the time constant is given by,
As t  ∞, the capacitor acts as an open circuit,
The general solution for the forced response of vC(t) is given by,

## Slide 51
Applying KVL around the loop,
After the switch is opened for t > 0,
Substituting ix, the equation becomes,
What about using the differential Equation (DEQ) approach directly – finding the integral?