## Slide 1: EEL 3004 Linear Circuits I Lecture #15 First Order LR Circuits - Natural responses without DC sources

## Slide 2: Lecture Objectives
The lecture today will focus on:
Introduction to switching RL circuits
Natural response of RL Circuits without DC sources
Examples

## Slide 3
If the circuit consists only of direct current and voltage sources (dc), and the switch has been closed or opened for long time, then the capacitor behaves as an open circuit, and the inductor behaves as a short circuit.
RLC circuits with DC sources and NO Switching
(Steady-state)
Under DC conditions – the circuit has been undisturbed for a long time

## Slide 4
The natural response for an RL circuits are obtained when the external independent source is set to zero or removed as shown below.
For the natural responses to exist it is required that the inductor have energy stored in it at the moment of switching and the equivalent RL circuits are obtained.
After certain action (switching):
Natural Response RL circuits
No External source
R’s and L’s Only
This circuit will responds naturally due to its L &R equivalent values.
We call it natural response or transient response.
Our goal to find the voltages, currents and power after t > 0.

## Slide 5
IMPORTANT DEFINITIONS
Natural Response of LR circuits
For t < 0, we let
For t > 0, we let
Therefore, for the inductor has these conditions met all the time:
=

## Slide 6
Any given resistive-capacitive circuit without external independent DC sources that can be reduced to a series equivalent L/R circuit.
The general solution for iL(t) is given,
General Natural Response of LR circuits
is the circuit time constant
= is the initial inductor value across in L.

## Slide 7
Any given resistive-capacitive circuit without external independent DC sources that can be reduced to a series equivalent L/R circuit.
The general solution for iL(t) is given,
General Natural Response of LR circuits
is the circuit time constant
R: The total resistance seen by the inductor
= is the initial inductor value
across in L.
Simplified circuit

## Slide 8
The natural response for an RL circuit is analogous to the natural response of an RC circuit
Consider the circuit where the switch moves from position ‘a’ to ‘b’.
Natural Response of RL circuits
=?

## Slide 9
The natural response for an RL circuit is analogous to the natural response of an RC circuit
Consider the circuit where the switch moves from position ‘a’ to ‘b’.
Natural Response of RL circuits

## Slide 10
The initial inductor current for t = 0- right before the switch is moved from ‘a’ to ‘b’, is given by,
Applying KVL around the parallel RL circuit,
Natural Response of RL circuits
Since the inductor current doesn’t change its value instantaneously
An ordinary first-order differential equation with constant coefficients

## Slide 11
It can be easily shown that the general natural response of iL(t) is given by,
Natural Response of RL circuits
Where iL(0) = Io is the initial inductor current, and the time constant,

## Slide 12
The voltage across the resistor is given by,
The instantaneous power delivered to R,
And the energy dissipated in R,
Natural Response of RL circuits

## Slide 13
The plot for the natural response of an RL circuit,
Natural Response of RL circuits

## Slide 14
Example
Initially the switch has been in position ‘a’ for a long time. At t = 0, the switch is moved to position ‘b’. Determine for t > 0:
  The currents iL(t) and iR3(t) and voltage vR3,
  The power dissipated in R3,
  The initial energy stored in L,
  The total energy delivered to R3,
  The percentage of energy dissipated in R3.
Variable | Values | Unit
Io | 2 | A
Ro | 2 | Ω
R1 | 8 | Ω
R2 | 5 | Ω
R3 | 4 | Ω
L | 0.5 | H

## Slide 15
The key is to find the for after the switch is closed, i.e. for .
Once we solve for then all the currents, voltages, power and energy can be expressed in terms of .
The inductor current is known as state variable
Solution A – Use the General Formula – short cut
The solution approach:
Let us use two possible solution methods:
Solution B – Use differential Equation (DEQ) approach directly – finding the integral

## Slide 16
The general solution (natural response) for iL(t):
Where,
is the initial inductor current
given by
Solution A – Use the General Formula
is the equivalent resistance seen by the inductor

## Slide 17
For t < 0 the inductor acts like a short circuit,
Applying KCL at the top node yields,
Hence,
Since the current in the inductance doesn’t change instantaneously,
Solution A – Use the General Formula
(1) Need to find

## Slide 18
For t > 0, the equivalent circuit is shown below
Simplified equivalent circuit, where
So, by inspection the time constant is:
(2) Need to find

## Slide 19
Recall for t>0, we have this DEQ,
Integrating both sides,
Raising both sides of the equation to the power of e,
Solution B – Use differential Equation approach directly applied to the DEQ below,
Need to find K !!
Notice this is equal to

## Slide 20
Evaluating the above equation att = 0,
Yes
Yes
The natural response is given by,

## Slide 21
The current in R3 can be found by current division,
And the voltage across R3is given by,

## Slide 22
The power dissipated inR3 is given by,
The initial energy stored in the inductor is,

## Slide 23
The total energy delivered toR3 is,
The percentage of energy dissipated in R3 is,

## Slide 24
Example
Initially the switch has been in position ‘a’ for a long time. At t = 0, the switch is moved to position ‘b’. Determine for t > 0:
  The currents iL(t) and iR3(t) and voltage vR3,
  The power dissipated in R3,
  The initial energy stored in L,
  The total energy delivered to R3,
  The percentage of energy dissipated in R3.
Variable | Values | Unit
Vo | 24 | V
Io | 6 | A
Ro | 2 | Ω
R1 | 8 | Ω
R2 | 5 | Ω
R3 | 4 | Ω
L | 0.5 | H

## Slide 25
For t < 0, we use the circuit to find
Solution – Use the General Formula
Use any analysis method to solve for
For t<0.

## Slide 26
For t < 0 the inductor acts like a short circuit,
Applying source transformation,
Solution – Use the General Formula

## Slide 27
Applying KCL to the single-node circuit yields,
It can be seen that,
Solving for iL(0) yields,
Since the current in the inductance doesn’t change instantaneously,
Assign v across all parallel branches

## Slide 28
finding the Thevenin total resistance seen by the inductor,
RTh is given by,
For t > 0, we use the circuit to find :

## Slide 29
And the time constant,
The solution for iL(t) is given by,

## Slide 30
The voltage across R3 is given by,
The current in R3 is given by,
+
-

## Slide 31
The initial energy stored in the inductor is,
The power dissipated in R3 is given by,

## Slide 32
Where,
The total energy delivered to R3 is given by,
The percentage of energy dissipated in R3 is,

## Slide 33
Example
The switch in the circuit has been in position ‘a’ for a long time. At t = 0, the switch is moved to position ‘b’. Find the current io(t) for t > 0,
Variable | Default | Unit
Io | 25 | mA
Ro | 100 | Ω
R1 | 200 | Ω
R2 | 150 | Ω
L | 10 | mH
α | 3 | -

## Slide 34
For t < 0 the switch has been open for a long time allowing the inductor to act like a short circuit,
Applying KCL at the top node,

## Slide 35
For t < 0 the switch has been open for a long time allowing the inductor to act like a short circuit,
Applying KCL at the top node,

## Slide 36
For t < 0 the switch has been open for a long time allowing the inductor to act like a short circuit,
Applying KCL at the top node,
Solving for V1,

## Slide 37
For t < 0 the switch has been open for a long time allowing the inductor to act like a short circuit,
Therefore the current iL(0-) is,
Since the current through the inductor doesn’t change instantaneously,

## Slide 38
To find the time constant, we need to find RTh.
RTh seen by the inductor,
Using the test voltage method, we have

## Slide 39
Apply KVL:
Apply KVL:
From the above two equations, we have
Thus the time constant,

## Slide 40
Another way to find RTh
Using the test voltage method, we have
Therefor, is given by,

## Slide 41
Recall we have,
The general solutions is given by,
Note that the output current is given by,