## Slide 1: EEL 3004 Linear Circuits Lecture #1B Overview Course and Introductory Concepts

## Slide 2: Syllabus (Update)
Basis for Final Grade
There will be six Teaching Assistances (TA’s) assigned to the three EEL 3004 Sections.
Quiz: Quizzes will be conducted almost weakly in the last 10-15 minutes of the class. A missing a quiz will receive a zero!
Tests: 3 In-person tests worth 15% each will be conducted in person.
Final Exam: The in-person final exam is comprehensive and weights 25%.
Discussion: Students are expected to attend the discussion and based on the level of their participation a 0-5% weight will be assigned. More will be provided by your discussion instructor.
Assignments | Total Percentages
Discussion Session | 5%
Quizzes | 25%
3 Midterm Exams (3x15%) | 45%
Final Exam | 25%
Total | 100%

## Slide 3
Grading Scale
Ryan Baumgartner
(954) 415-8252
ryan.baumgartner@ucf.edu
Discussion UAL
Two Discussion Periods:
Fridays:
9:00 – 10:50 AM
12:00 – 1:50 PM
Syllabus (Update)

## Slide 4: Lecture Objectives
Academic Assignment - Reminder
About Electrical Engineering Profession
Circuit Theory
Lumped Element Method Assumptions
Practical Example – The iPhone

## Slide 5: Student Academic Activities
All faculty members are required to document students' academic activity at the beginning of each course. In order to document that you began this course, you must attend the first week and sign the attendance sheet. This academic assignment (signing attendance sheet) must be done no later than the first Friday of the semester. Failure to do so will result in a delay in the disbursement of your financial aid.
For more info, please visit:
http://teach.ucf.edu/support/

## Slide 6: Academic Assignment
Read Chapter 1 and History of Electricity & Computing, and answer the following Three Questions:
1) List five different disciplines of Electrical and Computer Engineering.
2) Who discovered the electron and when?
        3) Who defined the notion of bit and when?

## Slide 7: What is Electrical Engineering
Layers of the field of Electrical/Computer Engineering:
  The Physical laws
  Components
  Devices
  Circuits or Networks (EEL 3004)
  Systems
  Product development
  Commercialization
Science
Engineering
Business

## Slide 8: What is Engineering? EE?
Engineering is the purposeful use of science based on proven scientific theorems and concepts that are supported by mathematical formulations.
Electrical engineering is a highly diverse, multidisciplinary profession that covers all types of electrical circuits and systems including communications, power and energy, control, electronics and microelectronics, signal processing, computing, and optics and photonics.
Cellular Communication System

## Slide 9: Electrical Circuits and Models
Electric circuits are the building blocks of many of today’s electrical systems, where all communication signals are inputted, processed, stored, and transmitted, and where all power signals are generated, transmitted, and distributed.
Examples of commercial circuit boards

## Slide 10: Passive and Active circuits
Analog electric circuits classified as either passive or active:
  Passive electrical circuits: components/circuits/systems - on the average, these circuits always dissipate power
  Active Electrical Circuits: semiconductor devices - on the average they can generate power

## Slide 11: Examples of Passive Elements
  Components:
  Examples: Resistors, capacitors, inductors, transformers, voltage sources, three-phase transformers.
  Passive Devices:
  Diodes fuses

## Slide 12: Examples of Passive Elements
  Circuits: Filter circuits, voltage dividers, ladder networks, bridge networks.
  Systems: Heater, toaster, tuner, battery charger, keyboard.

## Slide 13: Examples of Active circuits
These circuits are on average able to deliver power or amplify the current, voltage, or power by changing the voltage and current signals.
Devices - transistors
Integrated Circuits (IC)
circuits

## Slide 14: Examples of Active Elements
  Circuits: Voltage amplifiers, differential pairs, integrators, active filters.
  Systems: Stereo systems, power supplies, microphones.

## Slide 15: Electrical Circuit Analysis
This course only deals with the analysis and design of passive, linear, and analog circuits that are powered both by direct current (DC) alternating current (AC).
All electrical systems behaviors change as the frequency of the system changes.
Understanding frequency and its impact on circuit analysis, we need to understand the electromagnetic field - The Electromagnetic Frequency Spectrum
We need Maxwell’s equations. They give the fundamental foundation and framework for understanding electrical systems.

## Slide 16: Electromagnetic Frequency spectrum

## Slide 17: Electromagnetic frequency spectrum
Our Frequency of interest
Then, what are the frequencies of interest?

## Slide 18: Lumped Parameter Approach Assumptions
The application of circuit theory to analyze and design electrical circuits is simplified by the lumped parameter approach of circuit models.
The following three basic assumptions are made so the physical electrical system can be analyzed by using circuit theory instead of electromagnetic field theory:
  Current flow in the circuit will result in zero electric charge variation with respect to time at any given point in the circuit at all times (no electric charge leakages to the air).
  Current flow in the electrical circuit will produce zero variation in the magnetic flux with respect to time in parts of the circuit. (no magnetic field leakages to the air).
  All electric signal frequencies that flow in the circuit are assumed to be much smaller than the electromagnetic wave frequencies (ideal component behavior at low frequency)

## Slide 19: Lumped Parameter Approach Assumptions
Steps of modeling electric systems from applying Maxwell equations to applying simple circuit theory techniques.
Approach to Simplified Circuit Theory
Simpler

## Slide 20: Lumped Parameter Approach: Simplify Circuit Theory
Physics
Engineering

## Slide 21: Lumped Parameter Approach Assumptions
A list of physical electrical components, devices, circuits, and systems, and their corresponding idealized lumped element abstraction.
Examples of physical quantities with their equivalent lumped representation

## Slide 22: Lumped Parameter Approach Assumptions
Examples of the most-commonly used lumped representation in circuits
Resistor
Capacitor
Diode
Variable Resistor
LED
Transistor

## Slide 23: Example of the Lumped Element Method
A simple physical electrical network can be used to illustrate the usefulness of applying the above three assumptions.
Three Batteries – Vbattey Source
Light bulb #1 – resistor LB1
Light bulb #2 – resistor LB2
Switch – Symbol S shown
Analysis: How much current, voltage and power in each element?
Design: Make another circuit with three
bulbs circuit.

## Slide 24: Physical Elements become a Lumped Circuit Element
Having verified that the three assumptions hold, the circuit can be redrawn as a connection with three lumped parameters:

## Slide 25: Circuit Analysis
Next we carry t he circuit analysis on the simplified equivalent Lumped Circuit:
* Circuit Currents and Voltages: i, v1 and v2
* Calculate Power in each component
Circuit Analysis means to Find:

## Slide 26: Example of the Lumped Element Method
Assumption 1: No charge is depleted or accumulated while the current is traveling from the batteries through the lights, the electric switch and back to the batteries.
Assumption 2: the rate change of magnetic fluxes caused by the flow of all currents shown in (a) will be zero.
Assumption 3: The implication of the third assumption is not straightforward because the battery voltage represents a fixed voltage with zero signal frequency (dc).
iin = iout
ii,L1 = io,L1
ii,L2 = io, L2
iin = iout = ii,L1 = io,L1 = ii,L2 = io, L2 = i

## Slide 27: General Electrical Systems
A given system has a built-in process or intelligence that takes in inputs, process the inputs, and produces desired outputs.
  n inputs x1, x2, x3,…… xn
  m output signals y1, y2, y3,…….. ym
General block-diagram representation of a typical electrical system
Electrical Quantities
  Charge (q)
  Current (i)
  Voltage (V)
  Energy (W)
  Power (P)

## Slide 28
Electrical Signals

## Slide 29: AC vs. DC
Alternating Current (AC)
  Alternates back and forth in the positive and negative values.
  Distribution world-wide electricity: 60Hz or 50 Hz times a second.
Direct Current (DC)
  No Alternation, and current goes in one direction.
  Batteries and Circuits.
Direct Current
Tesla
Edison

## Slide 30: Electrical Signals
Unfortunately, because real-world physical components and devices are non-ideal, practical output signals are normally distorted in terms of shape, frequency, phase, and magnitude, and real components and devices can be lossy and noisy.
The better the electrical system is designed, the less the effect of non-idealities and distortion on the system performance.
Examples of practical (non-ideal or distorted) signals

## Slide 31: Analog vs. Digital
Analog describes a system whose values change continuously. Analog electrical current and voltage signals are continuous in time and can take on various magnitudes at different times.
Digital systems, on the other hand, do not change values continuously. Digital or discrete signals can take on discrete values at different quantized time intervals.
Analog vs. digital

## Slide 32: Analog vs. Digital
Significant improvements have been made in the process of converting analog signals to digital signals:
  discretization process: A process through which a single value is assigned to a range of values for a given parameter of interest. These sample electrical quantities are then called digital signals.
Analog vs. digital

## Slide 33: Analog vs. Digital
Significant improvements have been made in the process of converting analog signals to digital signals:
  discretization process: A process through which a single value is assigned to a range of values for a given parameter of interest. These sample electrical quantities are then called digital signals.
discretization process:

## Slide 34: Circuit Analysis and Design
Electrical engineers have developed a well-defined methodology for analyzing and designing electrical circuits and systems.
Science and engineering joint journey of product development

## Slide 35: Circuit Analysis and Design
Problem Solving:
  As a practicing engineer, you will spend most of your time solving problems (challenges) by designing and building products according to customer specifications, providing various engineering solutions, and working within a team.
The process of analysis begins with fully understanding the scope of the stated problem, then formulating the necessary assumptions and constraints, and then using mathematical tools and circuit theory to compute the desired parameters.
Circuit Analysis:

## Slide 36: Circuit Analysis and Design
  State the problem to be solved or design objective to be met.
  Identify any assumptions or constraints of the problem statement.
  Propose a possible design solution and find that solution.
  Check the viability of the solution and select the most appropriate solution to meet the objective in step1.
  Build and test the design. If the design objectives are not satisfactorily met, repeat the above steps.
Broadly speaking, today’s engineering design process follows five simple steps:
The process of design is more challenging and depends on the clarity of the statement and specifications of what is to be designed.
Circuit Design:

## Slide 37: Circuit Analysis and Design
Conceptual diagram of circuit analysis

## Slide 38: Circuit Analysis and Design

## Slide 39: Circuit Analysis and Design

## Slide 40: System of Units for Engineers
Used International System (SI) Units and their symbols

## Slide 41: System of Units for Engineers
Derived units based on the defined base SI units

## Slide 42: System of Units for Engineers
Common engineering standardized prefix multipliers and their symbols
Standardized prefix multipliers

## Slide 43: System of Units for Engineers
Common engineering standardized prefix multipliers and their symbols
Standardized prefix multipliers
Used in this
course

## Slide 44: Practical Example Apple iPhone Mesh Analysis – Voltage Amplifier
Voltage Amplifiers are electronic circuits that are used to amplify (enlarge) a weak input signal (voltage or current) and produce a stronger output signal (voltage or current).
Consumer Electronics: Radios, T.Vs., Cell phones, satellites, VCRs and DVD.

## Slide 45: Practical Example Apple iPhone Voltage/Power Amplifier
http://maltiel-consulting.com/iPhone_Components_maltiel_semiconductor-Update.htm#Inside_Apple_iPhone_3G

## Slide 46: Practical Example Smart iPhone Voltage/Power Amplifier
http://maltiel-consulting.com/iPhone_Components_maltiel_semiconductor-Update.htm#Inside_Apple_iPhone_3G

## Slide 47
Av: Stands for Voltage Gain
Commercial Product
Printer Circuit Board
Power Amplifier IC
Voltage Amplifier block Diagram
Mathematical Representation

## Slide 48
Practical Voltage amplifier

## Slide 49
http://electronics.stackexchange.com/questions/123879/amplifying-analogue-audio-from-an-iphone-docking-station
Practical Voltage amplifier – 400 W Audio Amplifier

## Slide 50
Practical Voltage amplifier – 400 W Audio Amplifier
http://electronics.stackexchange.com/questions/123879/amplifying-analogue-audio-from-an-iphone-docking-station
Resistor
DC Source
Diode
Transistors
Op Amp
Capacitor
Ground

## Slide 51
Simplified Common source amplifier with MOSFET Transistor
Highly Simplified Equivalent Circuit: MOSFET Voltage Amplifier
Input Signal
Output Signal
DC Source

## Slide 52
Simplified Common source amplifier with MOSFET Transistor
Highly Simplified Equivalent Circuit: MOSFET Voltage Amplifier
Input Signal
Output Signal
Active device
Transistor
DC Source
Drain (D)
Source (S)
Gate (G)

## Slide 53
Highly Simplified Equivalent Circuit: MOSFET Voltage Amplifier
Equivalent Small Signal model for a MOSFET Transistor
D
S
G

## Slide 54
Simplified Equivalent common source amplifier with MOSFET Transistor
Highly Simplified Equivalent Circuit: MOSFET Voltage Amplifier

## Slide 55
Highly Simplified Equivalent Circuit: MOSFET Voltage Amplifier
Simplified Equivalent common source amplifier with MOSFET Transistor
Using Circuit Analysis method in this course, we can solve for Av.

## Slide 56: ELECTRIC CIRCUITS
by
Issa Batarseh
University of Central Florida
Please send corrections or comments to Dr. Issa Batarseh
issa.batarseh@ucf.edu
Technical Electronic Book
(New Textbook under print by Pearson)

## Slide 57
Thank You !