## Slide 1: EEL 3004 Linear Circuits I Lecture #2 Electrical Quantities & DC power

## Slide 3: Lecture Objectives
Introduce Electric Quantities
  Charge (q)
  Current (i)
  Voltage (V)
  Energy (W)
  Power (P)
Cover several types of Currents
Power generation and dissipation
Type of depended sources – Examples
Electric Circuit Concepts including: circuit, branch, mesh, node…..

## Slide 4: Chapter 2
Electric Quantities: Charge, Current, Voltage, Energy, and Power
Circuit Elements
Electrical Network Concepts
Ohm’s Law
Kirchhoff’s Voltage and Current Laws
Circuit Simplification: Resistors in Series and Parallel
Basic Circuit Analysis
Measuring Current and Voltage
Problems
Fundamentals and Basic Concepts
(Skip)

## Slide 5: Electric Quantities
Electric quantities are charge (q), current (i), voltage (v), energy (w), and power (p).
Voltage must have sign polarities – or + be labeled across the element where measurement is taken.
Current must have arrow direction be labeled indicating the current direction in a given wire.
We use the Passive (positive) sign convention. The current assumed positive in the direction of the positive charges.

## Slide 6: Charge (q)
Charge on an electron, qe = -1.602x10-19 Coulombs (C).
Charge of a proton, qp = 1.602x10-19 Coulombs (C).
When a charge is in motion in a closed path, a current flows and electrical energy is transferred.
Pipeline of charge flow
The current assumed positive in the direction of the positive charges.
i

## Slide 7: Current (i)
The current, i(t), is the time rate of change of the electrical charge, q, passing through a predetermined area.
Unit for i(t) is coulombs (C) per second (s), which is the Ampere (A).
Current is positive if the direction indicates the flow of positive charge, which is opposite of the flow of negative charge (electrons).
Wire carrying a current

## Slide 8: Charge as function of Current
The current is given by,
To find q(t), we integrate both sides from -∞ to t.
q(0): initial value at t=0.

## Slide 9
Current Direction
or

## Slide 10: Current Flow in a battery

## Slide 11
Fig. 2.6 Analogy between current flow in electric circuit and water flow in water tank system

## Slide 12: Current Flow in a battery

## Slide 13
Exponential increasing
Exponential decreasing
Alternating Current (AC)
Unipolar square
Bipolar square
Types of Currents
Direct Current (DC)

## Slide 14: Types of Currents
Sinusoidally decaying
Non-Linear AC (magnitude)
Saw Tooth
Non-Linear AC (frequency)
Sinusoidal
Sinusoidally growing
Exponentially growing

## Slide 15
Exponential increasing
Exponential decreasing
Alternating Current (AC)
Unipolar square
Bipolar square
Types of Currents
Direct Current (DC)
Chapters 2-5
(all DC circuits)
Chapters 6-7
(RC-LR circuits)
Chapters 9-10
(all AC circuits)

## Slide 16
Charge Plot
Given the plot of the charge q(t), find the expression for i(t) and sketch it over the time intervals shown.
Example – Given Charge Plot

## Slide 17: Example – Charge current plots
Current plot
Charge plot
Solution

## Slide 18: Question
Given the plot of q(t) is drawn below,
Which corresponding plot for i(t) is the correct one?

## Slide 19: Question
Which plot is the correct i(t)?
q(t)
i(t)

## Slide 20: Question
Which plot is the correct i(t)?
q(t)
i(t)

## Slide 21
Consider the current expression entering a battery terminal is given as follows,
Example – Exponential Expression
Find the corresponds expression for the charge
Assum =0.
t>0

## Slide 22
For given
Example – Given Function
Solution:
We apply the following charge formula,
)
) C
Notice at t=0, =0 as expected.

## Slide 23
Example – Given Function
=16

## Slide 24: Voltage (v) and Energy (E)
The total work per unit charge associated with the motion of charge between two points, i.e., the rate of change of work or energy with respect to charge.
The unit for voltage (V) is volt.
The unit for work or energy (E) is Joules (J)
The unit for time is seconds (s)
The unite for charge is Coulombs (C).
If it takes one Joule to move one Coulombs of charge, the resultant potential (voltage) difference will be one volt.

## Slide 25: Energy and Power
Energy in the physical world is the capacity od doing work.
In electrical systems, energy is the multiplication of power (watts) and time (seconds).
Power is the amount of energy required or expended for a given unit of time.
            p
Where p is power in watts (W), w is energy in joules (J), and t is time in seconds (s).
So, in electrical networks, power is the product of voltage and current.

## Slide 26
Voltage polarity

## Slide 27: Energy and Power - Facts
The law of conservation of energy states that the total power generated in a given electrical network must equal the total power dissipated in the same network.
The sum of all absorbed positive power quantities must be equal to all dissipated negative power quantities.
Independent current and voltage sources will always deliver or generate power.
Resistors will always dissipate or waste power.
If p > 0 → power is dissipated or absorbed or lost
If p < 0 → power is generated or delivered or gained
Power can be positive or negative values (use the positive sign convention)

## Slide 28: Power Calculations

## Slide 29: Power Calculations

## Slide 30: Power in Resistors – Facts
p > 0 → power is dissipated or absorbed
P = +(IR x VR)
P is always positive in a given resistor
Resistors will always dissipate or waste power
VR
IR
VR
IR
P = +(IR x VR)

## Slide 31: Circuit Elements
The three main circuit elements are listed below:
Resistor: The relationship between the current passing through and the voltage across the element is linearly proportional.
(Ohm’s Law)

## Slide 32: Circuit Elements
The Potentiometer:
Fig. 2.31(a) Commercial potentiometer and (b) its two possible equivalent circuit representations
(a)
(b)
(c)

## Slide 33: Circuit Elements
Capacitor: The relationship between the current passing through and the voltage across the element is derivative proportional

## Slide 34: Circuit Elements
Inductor: The relationship between the current passing through and the voltage across the element is derivative proportional

## Slide 35
Ideal Voltage Sources – Dry Cell batteries

## Slide 36
Ideal Sources
voltage sources
Current sources

## Slide 37
Combining Sources
Voltages in Series
Currents in Series

## Slide 38: Power in voltage Sources – Fact
Voltage sources can produce/deliver power or absorb/dissipate power
p < 0 → power is generated or delivered
p > 0 → power is absorb or dissipate
(power is generated or delivered)
(Power is absorb or dissipate)

## Slide 39
Power Calculations in voltage sources
Charging
Charging
Discharging
Discharging

## Slide 40
Power Calculations in voltage sources
Charging
Discharging
Discharging
Charging

## Slide 41: Power in Current Sources – Fact
Current sources can produce/deliver power or absorb/dissipate power
p < 0 → power is generated or delivered
P = - (I) x (V) = - IV < 0
p > 0 → power is absorb or dissipate
P =+(I)x(V) = + IV > 0
+
V
-
-
V
+
Charging
Discharging

## Slide 42
Power Calculations in Current sources
Charging or Discharging

## Slide 43
Power Calculations in Resistors
Always dissipating power

## Slide 44
Dependent or Controlled Sources
(b) Voltage-controlled Current Source
(a) Voltage-controlled Voltage Source
(c) Current-controlled Current Source
(d) Current-controlled Voltage Source

## Slide 45
Examples of Circuit Models with Dependent Sources
The Bipolar Junction Transistor (BJT):
Example of using the BJT as a voltage amplifier known as common-emitter amplifier and its equivalent circuit

## Slide 46
Example of using the MOSFET as a voltage amplifier known as common-source amplifier and its equivalent circuits
Examples of Circuit Models with Dependent Sources
The Metal Oxide Semiconductor Field Effect Transistor (MOSFET):

## Slide 47
Examples of Circuit Models with Dependent Sources
Insulated Gate Bipolar Transistor (IGBT):

## Slide 48
The Silicon Controlled Rectifier (Thyristor):
Examples of Circuit Models with Dependent Sources

## Slide 49
Example of using the Op Amp as a non-inverting voltage amplifier
Examples of Circuit Models with Dependent Sources
The Operational Amplifier (Op Amp):

## Slide 50
Electrical Network Concepts
Electric elements
Branches
Nodes
Circuit Loops
Grounds

## Slide 51
Redrawing Nodes

## Slide 52
Electrical Network Concepts – Mesh loops
Mesh is a single loop that contains no other loops within it.
This is a mesh loop

## Slide 53
Examples Mesh Loops
Loops 1 and 2 are mesh loops
Loop 3 is NOT a mesh loop
since loops 1 & 2 are inside it.
Loops 1,2,3,4 are mesh loops
Loop 5 is NOT a mesh loop
since loops 1,2 & 4 are inside it.
Loop 5

## Slide 54
Example – DC Power
Solution:
Find the power for elements (state whether power is absorbed or delivered )
absorbed
absorbed
delivered