## Slide 1: EEL 3004 Linear Circuits I Lecture #5 Analysis of Single-loop and Single-Node Circuits

## Slide 2: Lecture Objectives
The main objective of this lecture is to discuss two special cases of circuit analysis:
  Analysis of Single-Loop Circuits
  Analysis of Single Node-Pair Circuits
Students will learn through Examples with independent and
dependent sources.
Students will learn the Intuitive Method: Circuit Reduction

## Slide 3: Simple Circuit Analysis Techniques
Chapter 3
Chapter Outline
Introduction
3.1 Analysis of Single-Loop Circuits
3.2 Analysis of Single-Node-Pair Circuits
3.3 Voltage and Current Division
3.4 Intuitive Analysis Method: Circuit Reduction
3.5 Voltage and Current Source Transformation

## Slide 4: Single-Loop Circuits
All elements of the circuits are connected in series.
Usually, one KVL equation needed around the loop unless dependent sources are used.
Single-Loop circuit with four elements

## Slide 5: Single-Loop Circuits
Assign a current in the single-loop with an arbitrary reference direction.
Label the voltage polarities for each resistive element with respect to the positive sign convention.
Write the KVL equation around the only loop.
Solve for the loop current.
Single-Loop circuit

## Slide 6: Example
Consider the single-loop circuit shown. Solve for the resistor currents in the circuit.
Single-Loop circuit
Variable | values | Unit
V1 | 10 | V
V2 | 15 | V
V3 | 5 | V
R1 | 5 | Ω
R2 | 12 | Ω
R3 | 18 | Ω

## Slide 7: Example
Because the circuit consists of a single loop, only one current variable, ix, is needed to be assigned.
Let us use the counter clock-wise direction for all elements:
Single-Loop circuit
The direction of the current for each individual resistor is chosen arbitrarily.

## Slide 8: Example
Solution:
The ix is the main loop current.
Select individual component currents iR1, iR2 and iR3.
Since this is a single loop it is clear that ix =iR1 =iR2 = iR3.
Because they have the same direction.

## Slide 9: Example
Applying KVL around the loop gives the following equation in terms of ix ,
Solve for ix to yield,
Solve for the resistor currents,
Note that all branch voltages and power in the circuit can be obtained once we solve for the loop current ix.
Single-Loop circuit

## Slide 10: Example
After assigning a current direction for each element, solve for the resistor currents in the circuit shown
Values:
Single-Loop circuit
Variable | Default | Unit
V1 | 18 | V
V2 | 10 | V
R1 | 5 | Ω
R2 | 25 | Ω
R3 | 15 | Ω
β | 5 | -

## Slide 11: Example
Solution:
Because the circuit consists of a single loop, only one current variable, ix, is needed to be assigned.
The direction of the current for each individual resistor is chosen arbitrarily.
Applying KVL around the loop gives the following equation,
Notice that,
Single-Loop circuit

## Slide 12: Example
Substitute vx in the above KVL equation to yield one equation in terms of ix, given by,
Solve for ix to yield,
Thus, solving for vx gives the following equation:

## Slide 13: Example
Given the single-loop circuit, determine the following:
  The voltages vx and vy.
  The power supplied by the voltage sources.
Single-Loop circuit
Variable | Default | Unit
V1 | 100 | V
V2 | 150 | V
R1 | 5 | Ω
R2 | 12 | Ω
R3 | 18 | Ω

## Slide 14: Example
After assigning current i, we write the KVL equation,
Solving for i,
The voltages can be easily expressed as,
Single-Loop circuit
Solution:
Assign a loop current, i, in the clockwise direction.

## Slide 15: Example
And,
The power supplied or absorbed by the voltage sources is given by,
(Supplied)
(Absorbed)

## Slide 16: Example
The net total power supplied by the circuit is given by,

## Slide 17: Example
The net total power supplied by the circuit is given by,
The 71 W are dissipated in the three resistors.
Let us Check:
PR=(R1+R2+R3) i2=( 5+12+18)(-1.43)2=+71 W

## Slide 18: Example
Given the single-loop circuit, determine the following:
  The voltages vx and vy.
  The power supplied by the voltage sources.
Single-Loop circuit
Variable | Default | Unit
V1 | 10 | V
V2 | 8 | V
R1 | 8 | Ω
R2 | 12 | Ω
R3 | 12 | Ω

## Slide 19: Example
Solution:
Assign a loop current, i, in the counter clockwise direction as shown.
Single-Loop circuit
We can simplify by finding the equivalent resistance for resistors R2 and R3.

## Slide 20: Example
Now writing the KVL equation,
Solving for i,

## Slide 21: Example
The voltages can be easily expressed as,
And,

## Slide 22: Example
The power supplied by the voltage sources is given by,
The total power supplied by the circuit is given by,
(Supplied)
(Absorbed)
(Supplied)

## Slide 23: Single-Node-Pair Circuits
All the circuit elements are connected across the same pair of nodes.
Usually one KCL equation needed to be written at one of the nodes.
Single-Node-Pair circuit
Upper node
Lower node

## Slide 24: Single-Node-Pair Circuits
Define a voltage v and arbitrarily assign its reference polarities across the node-pair.
Label the current direction in each resistive element according to the positive sign convention.
Write the KCL equation at one of the nodes.
Solve for the voltage v.
Single-Node-Pair circuit
+
-
v

## Slide 25: Example
For the circuit shown, solve for ix and all resistor currents,
Single-Node-Pair circuit
Variable | Values | Unit
I1 | 10 | A
I2 | 8 | A
R1 | 20 | Ω
R2 | 10 | Ω

## Slide 26: Example
Solution:
Assign voltage for vx across the parallel branches as seen,
Applying KCL to the upper node,
Single-Node-Pair circuit

## Slide 27: Example
Solving for vx yields,
The resistor currents iR1, iR2 and branch current ix shown below are given by,
Single-Node-Pair circuit

## Slide 28: Example
The current ix is given by,
Single-Node-Pair circuit

## Slide 29: Example
For the circuit shown, solve for ix and all resistor currents,
Single-Node-Pair circuit
Variable | Values | Unit
I1 | 10 | mA
I2 | 6 | mA
R1 | 30 | kΩ
R2 | 15 | kΩ
R3 | 15 | kΩ

## Slide 30: Example
Solution:
Assign voltage for vx across the parallel branches as seen,
Applying KCL to the upper node,
Single-Node-Pair circuit

## Slide 31: Example
Solving for vx yields,
The resistor currents iR1, iR2, iR3 and branch current ix shown below are given by,
Single-Node-Pair circuit

## Slide 32: Example
What about the current ix?
Single-Node-Pair circuit

## Slide 33: Example
For the circuit shown, solve for ix and all resistor currents,
Single-Node-Pair circuit
Variable | Values | Unit
I | 8 | mA
R1 | 12 | kΩ
R2 | 12 | kΩ
R3 | 6 | kΩ
β | 2 | -

## Slide 34: Example
Solution:
Assign voltage for vx across the parallel branches as seen,
Applying KCL to the upper node,
Single-Node-Pair circuit
But we know that:

## Slide 35: Example
Single-Node-Pair circuit
Solving for vx yields,
The resistor currents iR1, iR2, iR3 and branch current ix shown below are given by,
= V

## Slide 36: Example
Single-Node-Pair circuit
Check any node:
Check any node:

## Slide 37: Intuitive Method: Circuit Reduction
Reduce the number of components to an equivalent simplified circuit.
The final number of nodes and loops are significantly reduced.
Elements with currents and voltages of interest are left alone as given in the original circuit.
Does not follow a specific procedure, but rather depends on experience.

## Slide 38: Example
Use the circuit reduction method to find the current ix shown in the circuit.
Values:
Resistive circuit
Variable | Default | Unit
V | 18 | V
R1 | 5 | kΩ
R2 | 3 | kΩ
R3 | 8 | kΩ
R4 | 4 | kΩ
R5 | 7 | kΩ
R6 | 11 | kΩ

## Slide 39: Example
Solution:
To find the current ix, find the equivalent resistance as seen from terminals “a” and “b” as shown,
Original circuit
Equivalent circuit

## Slide 40: Example
Use the circuit reduction method to find the current ix shown in the circuit.
Values:
Resistive circuit
Variable | Default | Unit
I | 8 | A
R1 | 10 | Ω
R2 | 10 | Ω
R3 | 20 | Ω
R4 | 20 | Ω
R5 | 15 | Ω
R6 | 25 | Ω

## Slide 41: Example
Solution:
Because the current of interest is in the middle of the circuit, you combine the resistors in such a way that the R2 branch always remains by itself in the reduced circuit.
By combining R3 and R4 in parallel and R5 and R6 in series,
Reducing the circuit

## Slide 42: Example (Solution-cont’d)
Then you combine R2 in series with (R3//R4).
Then, R1 is combined in parallel with (R5+R6) as shown
Reducing the circuit
Reducing the circuit

## Slide 43: Example
For the circuit, given the values of Vo and all resistors, find:
The equivalent resistance, Req, seen between terminals “a” and “b”.
The current leaving the voltage source, i.
Resistive circuit
Variable | Values | Unit
Vo | 10 | V
R1 | 4 | kΩ
R2 | 1 | kΩ
R3 | 3 | kΩ
R4 | 4 | kΩ
R5 | 6 | kΩ
R6 | 6 | kΩ
R7 | 3 | kΩ
R8 | 5 | kΩ
R9 | 4 | kΩ

## Slide 44: Example
For the circuit, given the values of Vo and all resistors, find:
The equivalent resistance Req seen between terminals “a” and “b”.
The current leaving the voltage source, i.
Resistive circuit
Variable | Values | Unit
Vo | 10 | V
R1 | 4 | kΩ
R2 | 1 | kΩ
R3 | 3 | kΩ
R4 | 4 | kΩ
R5 | 6 | kΩ
R6 | 6 | kΩ
R7 | 3 | kΩ
R8 | 5 | kΩ
R9 | 4 | kΩ
Req

## Slide 45: Example (Solution)
Solution:
a) By inspection, R7, R8 and R9 are in series, R5 and R6 are in series and R2 and R3 as well.
Simplified circuit
The circuit is simplified as shown,

## Slide 46: Example 6 (Solution)
Moreover, the circuit can be simplified to the one shown,
Equivalent circuit
The total resistance seen by the voltage source Vo is 5.5 kΩ
Using Ohm’s law, we obtain,

## Slide 47: Example
Consider the circuit with all the parameters are given. Find the current i.
Resistive circuit
Variable | Values | Unit
Vo | 10 | V
R1 | 8 | Ω
R2 | 4 | Ω
R3 | 9 | Ω
R4 | 4 | Ω
R5 | 10 | Ω
R6 | 3 | Ω
R7 | 7 | Ω

## Slide 48: Example (Solution)
Solution:
We start by reducing the circuit as seen,
Equivalent circuit – Single Loop
Apply Ohm’s law,

## Slide 49: Example (Solution)
What if we ask for voltages ?

## Slide 50: Example (Solution)
What if we ask for voltage ?
Apply KCL:

## Slide 51
Check your answer – pick any loop
Let us assign as shown above. Then we must have
Notce, the current is given by,
So, we have
Now let us check your answer

## Slide 52: Example - Practice Quiz
(a) Determine the value for Ix. Show your work.
(b) Show that the total power developed equals the total power absorbed.

## Slide 53: Example - Practice Quiz
(a) Determine the value for Ix. Show your work.
(b) Show that the total power developed equals the total power absorbed.

## Slide 54: Example - Practice Quiz
Solution:
(a) Determine the value for Ix.

## Slide 55: Example - Practice Quiz
Solution:
(b) Calculate power in each element:
As expected, the total power is zero.

## Slide 56: 1841
The World’s First Programmer
British Mathematician and Computer Programmer Augusta Ada Byron (1815–1852) (later became Lady Lovelace)
https://www.linkedin.com/pulse/worlds-first-programmer-woman-lady-lovelace-issa-batarseh/
Reference my article on LinkedIn:
The World’s First Programmer was a Woman: Lady Lovelace