## Slide 1: EEL 3004 Electrical Networks Lecture #6 Simple Circuit Analysis Voltage and Current Division Formulas & Current-voltage source transformation

## Slide 2: Simple Circuit Analysis Techniques
Chapter 3
Chapter Outline
Introduction
3.1 Analysis of Single-Loop Circuits
3.2 Analysis of Single-Node-Pair Circuits
3.3 Voltage and Current Division
3.4 Intuitive Analysis Method
3.5 Voltage and Current Source Transformation

## Slide 3: Lecture Objectives
The lecture today will focus on Sections 3.3 and 3.4:
* Present two simple, but important, formulas:
  Voltage Division
  Current Division
Two simple practical analysis methods:
Voltage source to current source transformation to obtain single-­‐node-­‐pair or single node circuits

## Slide 4: Voltage Division
Two conditions must be met to apply what is known as Voltage Division:
1) All the resistors being used in the formula share the same current.
AND
2) The voltage being divided is applied across all the resistors used in the division formula.
Simple circuit with two resistors in series

## Slide 5: Voltage Division
Simple circuit with two resistors in series
The voltage across a given resistor is equal to that resistor divided by the total of series-connected resistors multiplied by the applied voltage.
In this case, we apply Voltage Division formula:

## Slide 6: Voltage Division
In this case, we apply Voltage Division formula:
Apply KVL,
Check:

## Slide 7: Voltage Division
Assuming the following current direction and voltage polarities,
Applying KVL to the circuit below,
Simple circuit with two resistors in series
Apply Ohm’s law:
Solving for yields,
Therefore, vR1 and vR2 are given by,

## Slide 8: Invalid Examples of Voltage Division

## Slide 9: Invalid Examples of Voltage Division
Or

## Slide 10: Invalid Examples of Voltage Division

## Slide 11: Invalid Examples of Voltage Division

## Slide 12: Invalid Examples of Voltage Division

## Slide 13: Invalid Examples of Voltage Division

## Slide 14: Voltage Division Formula
In series-connected resistors, the voltage across a given resistor is equal to that resistor divided by the total of series-connected resistors multiplied by the total voltage across the total of series-connected resistors.
Simple circuit with two resistors in series

## Slide 15: Example
For the circuit given, find the voltages across the resistors by using the voltage division formula.
Values:
Circuit with three resistors in series
Variable | Default | Unit
Vs | 18 | V
R1 | 5 | Ω
R2 | 10 | Ω
R3 | 15 | Ω

## Slide 16: Example
Short Cut Solution – Direct application of voltage division formula:
Check:

## Slide 17: Example
Standard Solution – Using KVL in a Single-Loop
Assume the direction of the current and voltage polarities shown, because the current in each resistor is the same then,
Applying KVL to the loop yields,
Solving for i yields,
Assigning current direction and voltage polarities

## Slide 18: Example
Therefore, the voltages across the resistors are given by,
Assigning current direction and voltage polarities

## Slide 19: Example
Use voltage division to find the voltage across each resistor in the circuit.
Values:
Single-Loop circuit
Variable | Default | Unit
Vs | 18 | V
R1 | 25 | kΩ
R2 | 5 | kΩ
R3 | 10 | kΩ
R4 | 10 | kΩ

## Slide 20: Example
Solution:
The circuit can be redrawn as an equivalent circuit with three series resistors,
Applying the voltage division formula,
Equivalent circuit with assigned current and voltages

## Slide 21: Example
Because R3 and R4 are in parallel,
Equivalent circuit with assigned current and voltages

## Slide 22: Current Division
To apply current division make sure that the resistors being used all have the same voltage across.
Current division gives you a simple method to find the current in single node-pair circuits.
Two resistors in parallel

## Slide 23: Current Division
Current division is not as simple as voltage division, to make the equations for current division simpler, resistance is expressed in terms of its conductance values.
Consider the circuit below,
Two resistors in parallel
is
iR1
iR2
What fraction of is flows in each resistor?

## Slide 24: Current Division
Consider the circuit below,
Two resistors in parallel
Check: is=iR1+iR2
What fraction of flows in and
It can be shown the the applied current flows in and according to current division formulas:

## Slide 25: Current Division
We assign current directions as shown, because the voltage across each resistor in the parallel-connected resistors is v,
Current directions assigned
Applying KCL at the upper node connects all the resistors to yield
Substitute for v, and solve for iR1 and iR2, respectively,

## Slide 26: Current Division
The equations of iR1 and iR2 consist of dividing the reciprocals of resistors.
Therefore, some books use the conductance, G, to express the current division formulas as shown,
Where,
Current directions assigned

## Slide 27: Example
Use the current division method to find the current in each resistor in the circuit given.
Circuit with load resistance

## Slide 28: Example
Solution:
First, combine R3 and R4 in series,
Applying the current division formula,
Equivalent circuit
Where,

## Slide 29: Example
Find the voltage across the load resistor vL for the circuit using current division.
Circuit with load resistance

## Slide 30: Example
Find the voltage across the load resistor vL in terms of the circuit parameters for the circuit using current division.
i=?

## Slide 31: Example
Find the voltage across the load resistor vL for the circuit using current division.
Circuit with load resistance
i=?

## Slide 32: Example
Solution:
The current passing through resistor R2,
Using the current division formula,
the voltage across the load resistor, vL,
Circuit with load resistance

## Slide 33: Example 6 (Solution)
Moreover, the circuit can be simplified to the one shown,
Equivalent circuit
The total resistance seen by the voltage source Vo is 5.5 kΩ
Using Ohm’s law, we obtain,

## Slide 34: Source Transformation
Vs
R
a
b
Is
R
a
b
Between node (a) and (b):
Voltage source Vs in series with resistor R can be replaced by a current source Is in parallel with R and vice versa.
Condition:

## Slide 35
Vs
R
a
b
VL
RL
IL
Is
R
a
b
VL
RL
IL
If the voltage is reversed, the we have

## Slide 36
Example
The two circuits below are equivalent (the same) Show that the two circuits have the same current value.
10
Apply the voltage division formula:
Apply Ohm’s Law
Apply the current division formula:
Apply Ohm’s Law

## Slide 37
Example – Use source transformation to find io
Apply KVL:
Solve for

## Slide 38
Example
Use the source transformation method to solve for all currents in the circuit.
Variable | Values | Unit
I | 8 | A
R1 | 5 | Ω
R2 | 15 | Ω
R3 | 10 | Ω

## Slide 39: Solution
Let us transform the current source I to voltage source:
IR3
Apply KVL:
Solve for

## Slide 40: Solution
The current in R1 and R2 is equal to ia
KCL at node va:
iR = I + ia
3
= 8 + (−2.7)= 5.3 A
Note: After using the source transformation, we can go back to the original circuit to find other values of current and voltage.

## Slide 41
Use the current-­‐to-­‐voltage transformation method to solve for all currents in the circuit.
Example
Variable | Values | Unit
V | 10 | V
I | 8 | A
R1 | 5 | Ω
R2 | 15 | Ω
R3 | 25 | Ω

## Slide 42
KVL:
= 9.4 Ω
= R2 // R3
Req
− V + R1ia + Req ia − IReq = 0
= 5.9 A
R1 + Req
IReq + V
ia =
Solution

## Slide 43
KCL at node va:
ia = I + iR
eq
= −2.1 A
iR = ia − I
eq
Next, obtain the individual currents in R2 and R3 by using Ohm’s
= −19.6 V
Req
= iR
vR = vR = vR
2 3 eq
eq
= −1.3 A
R2
R2
The current in R1 is equal to ia
v v
i =
R2
= −0.78 A
R3
i =
R3
R3
Solution

## Slide 44
For the circuit below find the currents , and as shown.
Example-Application of voltage and current division

## Slide 45
Apply voltage division:
Solution-Application of voltage and current division
Apply current division:

## Slide 46
Apply voltage division:
Solution-Application of current source transformation
Apply Current-source transformation:
Apply voltage division:
Since the voltage is also across the :

## Slide 47: 600 BC
Static Electricity perceived by Thales of Miletus
It is said that the Greek philosopher Thales of Miletus was the first known experimentalist on the static of electricity when he rubbed a rod of amber with cat's fur to attract light objects like feathers.
Thales of Miletus - Greek philosopher ( 624 BC – 546 BC)