## Slide 1: EEL 3004 Linear Circuits I Lecture #7 (Chapter 4) Advanced Circuit Analysis – Nodal methods

## Slide 2: Lecture Objectives
Chapter 4
Advanced Circuit Analysis Techniques
1) Voltage Node analysis
2) Mesh Current Analysis

## Slide 3: Lecture Objectives
The lecture today will focus on:
The concept of node voltages vs. element voltages
Introducing Nodal Analysis of circuits with current sources.
The circuit can be analyzed completely by only KCL equations.
Explaining Nodal Analysis of circuits with voltage sources, solving using the supernode, and external resistor insertion.
Illustration through solving examples.

## Slide 4: Node Voltages vs. Element voltages
Closed loop
Element Voltages:
The voltage across elements like Vx ,Vy,Vz V1,V2
-V1+Vx+Vy+Vz -V2=0
Apply KVL

## Slide 5: Node Voltages vs. Element voltages
Element Voltages:
The voltage across elements like Vx ,Vy,Vz V1,V2
-V1+Vx+Vy+Vz -V2=0
Apply KVL
Node voltages Va and Vb
Node Voltages:

## Slide 6: Node Voltages vs. Element voltages
Closed loop
What are the voltage values at Va and Vb ?

## Slide 7: Node Voltages vs. Element voltages
Valid Question:
What is the voltage value of Vab as shown?
Vab= Va -Vb
-V1+Vab-V2=0
Apply KVL around the left lopp
Vab= V1 +V2

## Slide 8: Node Voltages vs. Element voltages
Place ground at Vb
What are the voltage values at Va and Vb ?
Va= V1 +V2
Vb= 0

## Slide 9: Node Voltages vs. Element voltages
Place ground at Va
What are the voltage values at Va and Vb ?
Vb= -V2 –V1
Va= 0

## Slide 10
The Potential Difference:
Important concept: The voltage (potential difference) is always measured between two nodes.
Each node is references to a Reference Node “r “ we call ground
Nodal Analysis – Important Concept
Consider any arbitrary two nodes in a circuit
Reference Node (ground)

## Slide 11
The Potential Difference in a given circuit:
Nodal Analysis – Important Concept
Ground (reference) = 0 V
vr=0
+
-

## Slide 12
I. Circuits without voltage sources (including current sources)
II. Circuits with voltage sources (including current sources)
Nodal Analysis Method

## Slide 13
The circuit can be described completely by the required number of independent KCL equations.
KCL is simply the algebraic summation of all currents entering each node is zero.
Nodal Analysis with Current Sources
The key is to express all currents in terms of the node voltage
variables

## Slide 14
Examples of expressing currents in terms of the
node voltage variables
Assuming all currents flowing into the node “x”

## Slide 15
Examples of expressing currents in terms of the
node voltage variables
Assuming all currents flowing out of the node “x”

## Slide 16
Examples of expressing currents in terms of the
node voltage variables
Assuming all currents flowing mixed direction into & out of the node “x”

## Slide 17
Examples of expressing currents in terms of the
node voltage variables
Assuming all currents flowing mixed direction into & out of the node “x”

## Slide 18
Examples of expressing currents in terms of the
node voltage variables

## Slide 19
Examples of expressing currents in terms of the
node voltage variables

## Slide 20
Examples of Expressing Voltage Sources in terms of the
node voltage variables

## Slide 21
Examples of Expressing Voltage Sources in terms of the
node voltage variables

## Slide 22
Nodal Analysis with Current Sources
Given a circuit with n-nodes and no voltage sources, we follow the following steps:
1. Select a reference node and label it as ground.
2. Assign node voltages va, vb, vc ,…to the remaining (n-1) nodes.
3. Write (n-1) KCL equations at the (n-1) nodes by using Ohm’s law to express branch currents in terms of the node voltages.
4. Solve the (n-1) equations simultaneously for the nodal voltages va, vb, vc…
The circuit can be described completely by the required number of independent KCL equations.

## Slide 23
Example
Use the nodal analysis method to find:
The voltage and current in each resistance, and
The power dissipated in all resistors.
Variable | Values | Unit
I1 | 6 | A
I2 | 2 | A
R1 | 2 | Ω
R2 | 4 | Ω
R3 | 3 | Ω

## Slide 24
Note that there are three nodes: a, b, c
a
Solution
Any of these nodes can be ground or reference node (set to zero)
Let us consider three possible solutions:
Solution A – Set the ground node at c
Solution B – Set the ground node at b
Solution C – Set the ground node at a

## Slide 25
Nodal Analysis with Current Sources
Given a circuit with n-nodes and no voltage sources, we follow the following steps:

## Slide 26
Nodal Analysis with Current Sources
Given a circuit with 3-nodes and no voltage sources, we follow the following steps:
1. Select a reference node and label it as ground – set node c to zero voltage.
c

## Slide 27
Nodal Analysis with Current Sources
Given a circuit with 3-nodes and no voltage sources, we follow the following steps:
1. Select a reference node and label it as ground.
2. Assign node voltages va, and vb since we have only two nodes (n=2).
Two nodes: va and vb
c

## Slide 28
Nodal Analysis with Current Sources
Given a circuit with 3-nodes and no voltage sources, we follow the following steps:
1. Select a reference node and label it as ground.
2. Assign node voltages va, and vb since we have only two nodes (n=2).
3. Write 2 KCL equations at the 2 nodes (nodes va and vb ) by using Ohm’s law to express branch currents in terms of the node voltages.
Resistor currents can be assigned
KCL at node ‘a’:
KCL at node ‘b’:
(1)
(2)

## Slide 29
Given a circuit with 3-nodes and no voltage sources, we follow the following steps:
1. Select a reference node and label it as ground.
2. Assign node voltages va, and vb since we have only two nodes (n=2).
3. Write 2 KCL equations at the 2 nodes by using Ohm’s law to express branch currents in terms of the node voltages.
4. Solve the 2 equations simultaneously for the nodal voltages va, vb.
Nodal Analysis with Current Sources
Writing KCL at nodes va and vb:
(1)
(2)
Solving for va and vb,

## Slide 30
The current through the resistors,
The voltage across the resistors,
The power dissipated in the resistors,
Solve for the resistor currents:
Ground

## Slide 31
KCL at nodes ‘a’ and ‘b’:
Solving for va and vb,
Ground
Solution B – Ground Moved as follows:
(1)
(2)

## Slide 32
The current through the resistors,
The voltage across the resistors,
The power dissipated in the resistors,
Ground
Note: Same answers as Solution A
Solution B – Ground Moved as follows:

## Slide 33
KCL at nodes ‘a’ and ‘b’:
Solving for va and vb,
Ground
Solution C – Ground Moved as follows:

## Slide 34
The current through the resistors,
The voltage across the resistors,
The power dissipated in the resistors,
Ground
Note: Same answers as Solution A
Solution C – Ground Moved as follows:

## Slide 35
Solution A
Solving for va and vb:
Solution B
Solution C

## Slide 36
Example
Use the nodal analysis method to find:
The voltage and current in each resistance, and
The power dissipated in all resistors.
Variable | Values | Unit
I1 | 6 | A
I2 | 2 | A
R1 | 2 | Ω
R2 | 4 | Ω
R3 | 3 | Ω
g | 0.5 | Ω-1

## Slide 37
KCL at nodes ‘a’, ‘b’, and ‘c’:
Solution:
(1)
(2)
(3)
U , , and !!!
But we only have 3 equations (1)-(3)?

## Slide 38
KCL at nodes ‘a’, ‘b’, and ‘c’:
Solution:
(1)
(2)
(3)
U , , and !!!
But we only have 3 equations (1)-(3)?
Answer: we can express in terms of and
(4)

## Slide 39
A?
Solution:
Apply KVL around , , and as follows:
=
(4)
Now substitute for Eq. (4) into Eqs. (2) and (3) and then solve for , ,

## Slide 40
Solving for va, vb, and vc,
Solution
If you are asked to find voltage
=

## Slide 41
The voltage across the resistors is,
The current through the resistors is,
The power dissipated in the resistors is,
Solution:

## Slide 42
Pick any node and write KCL
Check your Solutions
Let us pick the ground node:
?
6 – 4 – 2 =0. OK

## Slide 43
II. Circuits with voltage (including current sources)
Nodal Analysis Method

## Slide 44
The number of required KCL equations is reduced.
Voltage at the node is directly assigned to the voltage source with respect to the reference node.
Nodal Analysis with Voltage Sources
Notice:
The current in this branch is not known to write KCL

## Slide 45
The number of required KCL equations is reduced.
Voltage at the node is directly assigned to the voltage source with respect to the reference node.
Nodal Analysis with Voltage Sources
KCL at the supernode:

## Slide 46
If the voltage source has a resistor in series, then by using source transformation we may replace it by an equivalent current source
Nodal Analysis with Voltage Sources in Series with a resistor

## Slide 47
If the voltage source has a resistor in series, then by using source transformation we may replace it by an equivalent current source
Nodal Analysis with Voltage Sources
Hence, the supernode is eliminated.

## Slide 48
Example
Write the correct KCL equations at each node for the given circuit

## Slide 49
Solution:
KCL at nodes ‘a’, ‘b’ and ‘c’:
Assigning three node voltages and reference node.
Because we have a voltage source, the number of nodes can be reduced.
Assign three variable nodes: va, vb, and vc ; and the ground node.
Only two equations need to be solved for !

## Slide 50
Example
Find the voltages, currents and power for each of the resistors.
Variable | Values | Unit
V1 | 20 | V
V2 | 10 | V
R1 | 18 | Ω
R2 | 14 | Ω
R3 | 6 | Ω
α | 0.2 | -

## Slide 51
Example
Find the voltages, currents and power for each of the resistors.
Variable | Values | Unit
V1 | 20 | V
V2 | 10 | V
R1 | 18 | Ω
R2 | 14 | Ω
R3 | 6 | Ω
α | 0.2 | -
Supernode

## Slide 52
KCL at the supernode ‘bc’:
The current ix is given by:
By inspection the voltage va is given by:
The voltage across V2 is given by:

## Slide 53
The resistors current,
Solving for vb, and vc,

## Slide 54
The power dissipated in the resistors,
The voltage across the resistors,

## Slide 55
Example
Find the voltages and currents for all the resistors.
Variable | Values | Unit
V | 5 | V
I1 | 12 | A
I2 | 8 | A
R1 | 10 | Ω
R2 | 6 | Ω
Solutions:
Solution A - Use the Supernode Method
Solution B - Use the external resistance method

## Slide 56
Solution
Assign nodes va and vb
Solution A) Use the Supernode Method
Notice we cannot write KCL at nodes va and vb since they are connected to a volage source.
Use this super node
Apply KCL around the shaded node,
Notice that,
- (1)
Solving Eqs. (1) and (2) for the voltages va, and vb,

## Slide 57
Insert an external resistor ro in series with the Voltage source V.
Solution B) Use the external resistance method
The approach:
Add small ro then set it to zero at the end!

## Slide 58
Applying a Voltage-to-Current source transformation:
Assign nodes va and vb
Solve for nodes va and vb then set ro=0!
Solution

## Slide 59
Solving for the voltages va, and vb,
Applying KCL at nodes va, and vb,
Solution
Solving for the voltages va, and vb,
Set ro=0

## Slide 60
The current passing through the resistors is,
The voltage across the resistors is,
Solution
18.2
1.8

## Slide 61
Design Examples- Voltage Node Analysis.
Use the node voltage analysis to design the circuit shown so that VR1=2 and VR2=6 V.
Consider R2= 50 Ω and I=6 A.
VR1
VR3

## Slide 62
Design Examples- Voltage Node Analysis.
Use the node voltage analysis to design the circuit shown so that VR1=2VR2=6 V.
Consider R2= 50 Ω and I=6 A,.
Assign nodes 1 and 2 as shown
Solution:
VR1
VR3

## Slide 63
Given R2= 50 Ω,
We design for:
R3= 50 Ω
R1= 1 Ω,
Solution:

## Slide 64
Examples: Applying Nodal Analysis

## Slide 69: 2025+
What is next?
You?