## Slide 1: EEL 3004 Electrical Networks Lecture #18 Applications – Electro Static Discharge (ESD) – Ch. 5

## Slide 2
Electro Static Discharge (ESD)
RC Transients - Practical Relevance
Electro Static Discharge (ESD) is a dangerous phenomenon in electrical systems that can destroy electronic components, devices and systems. ESD occurs when two physical bodies (human body and electric circuits) of different electrical potential come into close proximity, and the electrostatic charges start to transfer between the two bodies.
The sudden electrostatic discharge can produce large current or voltage surges, causing severe damage to electronic parts.
The current surges can cause overheating of the electric package, silicon and metal parts beyond their melting point causing permanent damage
The ESD can originate from several sources, but one of the most common causes of electrostatic damage is the direct transfer of the electrostatic charge from the human body to a device.

## Slide 3
Electro Static Discharge (ESD)
RC Transients - Practical Relevance
Fig. 5.1 (a) sudden electrostatic discharge, (b) current or voltage surges, causing severe damage to electronic parts, (c) human touch without insulation, (d) permanently damaged IC

## Slide 4
Electro Static Discharge (ESD)
The ESD is harmless to humans, but will cause severe damage to sensitive, modern electronic equipment. Several techniques are used to preventing ESD. The best methods are to use a wrist strap, a grounding mat, ESD safe shoes, and a grounding workbench as shown in Fig. 5.2.
Fig. 5.2 Methods to prevent ESD from damaging electronic components

## Slide 5
Electro Static Discharge (ESD)
There are many commercial ESD Test Systems available on the market to test the immunity of electronic devices to ESD. The device emulates the origin of the ESD in the human body and then identifies how immune the electronic device is to the charge. Figure 5.3 shows one well known commercial ESD Test System, model # ESD3000.
Fig. 5.3 ESD3000 – Modular Handheld Tester for Electrostatic Discharging Testing

## Slide 6
Electro Static Discharge (ESD)
The Human Model
When a charged human body touches an electronic part, the electrostatic charge stored inside the human body discharges into the electronic part.
Equivalent Capacitance is the human body capacitance, is the discharging human resistance and the Device Under Test (DUT) is the electronic part.
Typically, the human body capacitance is charged with a static charge. When it is connected suddenly to a device under test, the discharge begins with a large spike current that exponentially decays.

## Slide 7
Electro Static Discharge (ESD)
The Human Model
Figure 5.4: The ESD phenomenon where (a) a human body model causes an electric discharge to transfer from the body to a “device under test” (DUT), (b) equivalent circuit model

## Slide 8
Electro Static Discharge (ESD)
Calculating the Discharge Current:
Under these standard conditions, it is assumed that the body’s capacitance is charged to 2kV. The current passing through the circuit is given by the equation of the RC circuit,
Where,
Using the typical values, the discharge current is given by,
Where .

## Slide 9
Electro Static Discharge (ESD)
The Discharge Current:
Figure 5.5: discharge current waveform
The peak power released during the voltage strike equals