## Slide 1
EEL 5245 POWER ELECTRONICS I Lecture #10
Ch. 3: Power System Basics and Sinusoidal Systems

## Slide 2: Objectives
Review of Basic Power Concepts
  Efficiency-Practical Example
  Average and RMS Calculations
    Commonly observed waveform
Sinusoidal Systems
  Load Types
  Average, Reactive, and Apparent Power
  Power Factor
  Power Factor Correction
  3 Phase, 4 Wire Neutral Currents

## Slide 3
Power grid and various kinds of power plants

## Slide 4
Electricity form Generation to Home
http://waterheatertimer.org/What-is-3-phase-electric.html

## Slide 5
The instantaneous power, , is measured as the product of the instantaneous currant, , and the instantaneous voltage,
The unit of instantaneous power, , is watts (W).
Instantaneous Power

## Slide 6
Determining instantaneous power in transient dc, RLC circuits requires the use of the time domain expressions for capacitor voltage and inductor current.
Instantaneous Power

## Slide 7
Instantaneous circuits of steady state AC circuits
Assume all transient voltages and currents are gone (steady-state).
Assume the input voltage source and the corresponding source current given by
Where v and i are the voltage and current phase shifts.
Applying simple trigonometric identities, can be expressed as,
Hence, the resulting instantaneous input source power is given by,

## Slide 8
Instantaneous circuits of steady state AC circuits

## Slide 9
Instantaneous circuits of steady state AC circuits

## Slide 10
Instantaneous circuits of steady state AC circuits
Power to home from utility

## Slide 11
Instantaneous circuits of steady state AC circuits
Power back to utility

## Slide 12
Instantaneous circuits of steady state AC circuits
Average Power to home from utility
1000 W for one hour= kWh
1 kWh priced at $0.1-$0.13

## Slide 13
We notice that the instantaneous power delivered by, an ac sinusoidal source has two components:
  A constant or d.c. power,
  A time varying a.c. power,
3. Frequency is varying at twice the frequency of the voltage source, vS(t), i.e. the instantaneous power completes two cycle where each of vS and iS complete one cycle.
4. The phase shift (v - i) is the phase shift of the instantaneous power expressed as the difference between the voltage and current phase angles.
Instantaneous circuits of steady state AC circuits

## Slide 14: Average, Reactive and Apparent Powers
Power Flow from input-to-output
Unidirectional
Bi-directional

## Slide 15: Average and RMS Calculations
In modern power electronics converters, electrical parameters have periodic and nonlinear waveforms (steady state)
  Switch Current, Diode Voltage, Inductor Current, etc.
Both average and RMS values of these highly, nonlinear wave shapes are often needed for design
  Average is area under curve divided by period
  RMS used for power loss calculation
Given Periodic Function f(t):
Average of f(t):
Rms of f(t):

## Slide 16: Instantaneous and Average Power
Instantaneous Power: is point for point product of voltage and current
Average Power: “Useful” power is average of Instantaneous, Pavg (Real Power)
Apparent Power: is product of RMS values of voltage and current
RMS definition can be derived from instantaneous power average

## Slide 17: Average and RMS Calculations Nonlinear/Piecewise Wave shapes
Example of Boost DC-DC Converter

## Slide 18: RMS & Average Value Calculation
Discontinuous Conduction Mode (DCM)
Average Value:
RMS Value:

## Slide 19
Different time-line labeling

## Slide 20
Other common waveforms

## Slide 21: RMS & Average Value Calculation
Continuous Conduction Mode (CCM) – DC+Linear Ripple
Average Value:
RMS Value:

## Slide 22
RMS Value:
Detailed derivation of CCM Ripple Current
RMS & Average Value Calculation

## Slide 26
Comparing CCM and DC Rms Values

## Slide 28: Efficiency in Power Electronic Converters
Efficiency is one of the most significant figures of merit
  Can be used to judge overall performance of topology in many cases
Modern Power Electronic Converters have efficiencies approaching 100%
For in-class analysis, if power electronic circuit consists of ideal switches, transformers, and energy elements (L&C) efficiency is 100%
In Real World Circuits, losses play a significant role:
  Dominate Loss Mechanisms
    Semiconductor Switch Loss: Conduction and Switching
  Losses are a function of operating point

## Slide 29: Efficiency in “Real World” Power Electronics Circuits
Example – Power Factor Connections

## Slide 30: Sinusoidal Systems
Given source current and voltage:

## Slide 31: Sinusoidal Systems
Recall that the RMS value of any pure sinusoidal is peak divided by root 2
Phase shift in this diagram a result of reactive elements
  In this case, a capacitive load as I leads V
Real power is maximized when v(t) and i(t) are in phase since overlap is maximized
  Any relative shift between the two means real power is less than maximum while RMS is unaffected

## Slide 32: Sinusoidal Systems Purely Resistive Load
V(s)
I(s)
P(t)

## Slide 33: Sinusoidal Systems Resistive-Inductive Load
V(s)
I(s)
P(t)

## Slide 34: Sinusoidal Systems Resistive-Capacitance Load
V(s)
I(s)
P(t)

## Slide 35: Sinusoidal Systems Purely Inductive Load
V(s)
I(s)
P(t)

## Slide 36
Power Factor (PF)
A dimensionless quantity that gives a measure of device’s or a network’s ability to absorb or deliver average power from the maximum available source.
Maximum available power is the Apparent Power.
So, it is the ration of what is delivered in the average over what is maximum available.

## Slide 37
Power Factor (PF)
If all available VA power can be converted and used as average power by the given device, then the device exhibits unity power factor.
In order to correct the power factor i.e. make the phase angle between the load current and load voltage equal zero,
Power engineers add what is called power factor correction circuits which is capacitor circuit to count the lagging effect.
Power factor at the load side is the same as the Pf of the source side given they share the same terminals.
Hence, whether pf is a leading or lagging power factor, implies that the current is leading or lagging the voltage, respectively.

## Slide 38: Sinusoidal Systems-Power Factor
For the resistive load (Θ=0), both real and apparent power are Vrms*Irms
Irms is current load and power distribution system
For resistive load, power system capacity is most efficiently utilized
For any relative phase shift (i.e. Θ Not equal to 0), power system capacity more stressed that what is strictly necessary to deliver required real power to load
Power Factor is measure of how effectively power system is being utilized

## Slide 39: Sinusoidal Systems-Reactive Power
What makes up difference between apparent power and real power when pf<1
For any relative phase shift (i.e. Θ not equal to 0), additional circulating energy due to charging and discharging of system reactive elements
Reactive Power passed back and forth from source to load using system capacity but provides no real power to load (i.e. performs no work)

## Slide 40: Sinusoidal Systems Real, Reactive, and Apparent Power Related
Power Triangle above drawn for R-L load so if 0< Θ <90 we say power factor is “lagging”, since I lags V with an inductive load

## Slide 41: Sinusoidal Systems Power Factor
A dimensionless quantity that gives a measure of a device’s or a network’s ability to absorb or deliver average power from the maximum available source.
Maximum available is the Apparent Power.
So, it is the ratio of what is delivered in the average over what is maximum available.

## Slide 42: Sinusoidal Systems Power Factor Correction
Utility wants to provide minimum current necessary to meet customer Real (Average) power requirements
  Transmission lines have maximum capacity
  Higher current means more I2*R losses
Utilities will place capacitor banks in parallel with user loads at the remote location to make load look resistive to their generators
Impedance to improve pF

## Slide 43: Power Factor Correction

## Slide 44: Exercise 3.11 - Power Factor Correction
The power factor angle,
Complex Power
The average power and Reactive Power Q:
Solution:
Recall, that the complex power,
A
A
The impedance is obtained from,
(Inductive-Resistive impedance)

## Slide 45: Exercise 3.11 - Power Factor Correction
Now, what if we want to correct the power factor to 0.97. What should be the (reactive only) that need to be added?
The new power factor angle,
Hence, the additional that need to be added is given by,
(Capacitive impedance)

## Slide 46
Now, the total load impedance including the PF correction capacitor, is given by,
//
Finally, for a unity power factor (PF=1.0) we must add , resulting in C=3.51 mF.
=
Check:

## Slide 47: Sinusoidal Systems Power Factor Correction
Exercise 3.11 (simulation)
PF to 0.75

## Slide 48: Sinusoidal Systems Power Factor Correction
I - Correct PF to 0.97
PF=0.97

## Slide 49: Sinusoidal Systems Power Factor Correction
II - Correct PF to 1.0
PF=1.0
C=3.51 mF

## Slide 50: P.F. Example
Consider the following RL load circuit with poor input PF. Correct its input power factor unity

## Slide 53: Sinusoidal Systems Power Factor Correction

## Slide 54: Sinusoidal Systems Power Factor Correction