## Slide 1: EEL 5245 POWER ELECTRONICS I Lecture #14: Ch 4: Non-Isolated DC-DC Converters PWM Converters Buck Analysis (CCM)

## Slide 2
Midterm Exam
Oct. 30 (Monday)
Chapters 2,3 and Sections 4.1-4.4
In class with open notes and book

## Slide 3: Objectives
Overview of DC-DC Conversion
  Linear Regulators: Regulated vs. Unregulated
  Overview of Pulse Width Modulation Converters
PWM Converter Analysis Principles/Tools
Buck Converter Analysis (Continuous & Discontinuous Conduction Mode (CCM&DCM)
  Voltage Conversion Ratio (M=Gain)
  Average Input and Output Currents
  Output Voltage Ripple via Charge approximation
  Boundary Between CCM and DCM
Calculation Example
Analysis Verification by Simulation

## Slide 4: Classic Converter Topologies
Voltage Gain  M=V/Vg

## Slide 5: Analysis of Classic Converter Topologies
Analysis will assume lossless components
Exact steady state analysis would involve solution of nonlinear, 2nd Order system, we will simplify to a 1st Order System with:
  Since RC>>Ts, output voltage nearly constant over switching period
    Since ripple is assumed small, we assume Vo a constant during analysis (output cap not considered)
We assume analysis of converter takes place at after it has reached steady state
  Since steady state, average inductor voltage equals zero over switching interval (volt-sec balance)
  Since steady state, average capacitor current over one switching interval equals zero (charge balance)

## Slide 6: Analysis of Classic Converter Topologies
  Icavg=0 (Charge Balance)
The preceding concepts can be expressed in terms of mathematical relations.
These are tools for analysis:
  Pout=Pin (Power Conservation)
  iL(to)=iL(to+Ts) (Steady State)
  VLavg=0 (volt-sec balance)
  vC(to)=vC(to+Ts) (Steady State)

## Slide 7: Converter Analysis Principle Small Ripple Approximation

## Slide 8: Converter Analysis Principle Inductor Volt-Second Balance
Inductor defining relation :
Integrate over one complete switching period :
In periodic steady state, the net change in inductor current is zero :
Hence, the total area (or volt-seconds) under the inductor voltage
waveform is zero whenever the converter operates in steady state.
An equivalent form:
The average inductor voltage is zero in steady state

## Slide 9: Converter Analysis Principle Capacitor Charge Balance
Capacitor defining relation:
Integrate over one complete switching period
In periodic steady state, the net change in capacitor voltage is zero:
Hence, the area (or charge) under the capacitor current
waveform is zero whenever the converter operates in steady state.
The average capacitor current is then zero.

## Slide 10: Figures of Merit for the PWM DC-DC Converter
Classic Converter Analysis (CCM&DCM)
  Voltage Conversion Ratio (M=Gain)
    Use Inductor Volt-second balance
  Average Input and Output Currents
    Use waveform analysis and
    Capacitor charge balance and small ripple approximation (Icavg=0)
  Output Voltage Ripple via Charge approximation
    Small ripple approximation meeans all ac component of output current seen by capacitor, DC to load R
  Inductor current Ripple
    Derived from inductor current waveform
  Boundary Between CCM and DCM
    Concept of Critical Inductance derived from iL expressions

## Slide 11: Buck Converter
Switch Position 2 for allow for uninterrupted inductor current flow
LPF for smoothing of pulse for constant DC output
Capacitor hold a DC value for the load when switch in position 1 (Inductor current charge)
2nd Order-1 L, 1 C
Switch-diode implementation
Switch is in Position 1: S is on and D is off
Switch is in Position 2: S is off and D is on

## Slide 12: Buck Converter Analysis: Mode by Mode

## Slide 13: Buck Converter Analysis: Mode I
Inductor voltage
Small ripple approximation :
Solve for the slope :
The inductor current changes with an essential constant slope

## Slide 14: Buck Converter Analysis: Mode II
Inductor voltage
Small ripple approximation :
Solve for the slope :
The inductor current changes with an essential constant slope

## Slide 15: Buck Converter Analysis: Waveforms Start up Transient
2Ts
3Ts
iL(DTs)

## Slide 16: Buck Converter Analysis: Waveforms Inductor Voltage and Current

## Slide 17: Converter Analysis Principle Volt-Second Balance gives Voltage Gain, M

## Slide 18: Waveforms Input, Diode and Capacitor Currents

## Slide 19: Inductor Current Initial and Final Values
We need to find the values for iL(0) and iL(DTs) in terms of the
Converter parameters.
Let us label:
Output volage (V) : Vo
Input voltage (Vg): Vin
Switching period (Ts): T

## Slide 20: Buck Converter Analysis: Waveforms Average Input and Output Currents
By inspection from the plot for Iin,

## Slide 21: Buck Converter Analysis Using Average Current to get iLmin/iLmax

## Slide 22: Buck Converter Analysis Lcritical
Notice that there is a value when ILmin=0, hence the inductor become discontinuous – we enter what is called Discontinuous Conduction Mode (DCM):

## Slide 23: Buck Converter Analysis Concept of DC Transformer

## Slide 24: Inductor Current Ripple
In terms of the inductor,

## Slide 25: Output Voltage Ripple
It will be shown that by equating Q+=Q- we obtain,

## Slide 26: Buck Converter Analysis: Hand Calculation Example 4.2

## Slide 27
Example 4.2 Solution (cont’d)

## Slide 28
Example 4.2 Solution (cont’d)

## Slide 29: Example 4.2 Simulation Verification

## Slide 30: Simulation Verification Example 4.2-Startup
Time
0s
0.5ms
1.0ms
1.5ms
2.0ms
I(L)
V(Gate)
V(Output)
0
10
20
Vo= 15V

## Slide 31: Simulation Verification Example 4.2 Various Waveforms
Time
1.96ms
1.98ms
2.00ms
V(L:1,L:2)
-20V
-10V
0V
10V
Time
1.96ms
1.98ms
2.00ms
I(Cf)
-40mA
-20mA
0A
20mA

## Slide 32: Simulation Verification Example 4.2 Various Waveforms
Time
1.96ms
1.98ms
2.00ms
I(L)
4.90A
4.95A
5.00A
5.05A
Time
1.96ms
1.98ms
2.00ms
V(Output)
14.8V
15.0V
15.2V
(1.9819m,14.863)
(1.9954m,15.102)

## Slide 33: Example of Buck Converter Waveform

## Slide 34: Example of Buck Converter Waveform
For the first mode of operation, current iL is rising, we have this relation:
For the second mode of operation, current iL is falling, we have this relation:
Solution:

## Slide 35: Buck Converter Analysis: Waveforms Inductor Current Ripple
Solution (cont’d):