## Slide 1: EEL 5245 POWER ELECTRONICS I Lecture #4: Chapter 2 Switching Concepts and Semiconductor Overview

## Slide 2: Objectives of Lecture
Switch realizations
Objective is to focus on terminal characteristics
  Blocking capability
  Conduction direction
Device loss mechanisms
Qualitative relationships between
  On state resistance
  Breakdown Voltage
  Switching Time
Survey of some commonly available commercial products
Comparison of Switching Devices

## Slide 3: Switching Functions and Matrix Representation
nxm Switching Matrix

## Slide 4
Photovoltaic Applications - Four port Dual-PV-Battery LLC converter

## Slide 5
Photovoltaic Applications - Four port Dual-PV-Battery LLC converter

## Slide 6: Switch Classifications

## Slide 7: Switch Realizations-Power Diode
Passive means no active means of control
Device conducts in forward direction in response to positive forward voltages
Devices turns off with negative forward voltage

## Slide 8: Switch Realizations-BJT/IGBT
Active-controlled turn on and turn off
BJT conduct in forward direction in response to control current at C
IGBT conduct in forward direction in response to control voltage at C (wrt terminal 0)
Devices turns off when control signal removed

## Slide 9: Switch Realizations-MOSFET
Active-controlled turn on and turn off
MOSFETs conduct in forward direction in response to control voltage at C (wrt terminal 0)
Devices turns off when control signal removed

## Slide 10: Switch Realizations-SPST

## Slide 11: Switch Realizations-BJT and Diode

## Slide 12: Switch Realizations- Anti-parallel Diode
Usually an active switch,
controlled by terminal C
Normally operated as two-
quadrant switch :
Can conduct positive or
negative on-state current
can block positive off-state
voltage
provided that the intended on-
state and the off-state operating
points lie on the composite i-v
characteristic, then switch can
be realized as shown

## Slide 13: Switch Realizations- MOSFET Body Diode

## Slide 14: Switch Realizations- Bidirectional Voltage Blocking-SCR
Thyristor family also has this i-v characteristic
  Silicon Controller Rectifier (SCR)
  Gate Turn Off Thyristor (GTO)
Usually an active switch,
controlled by terminal C
Normally operated as two-
quadrant switch :
Can block positive off-state
voltage
Provided that the intended on-
state and the off-state operating
points lie on the composite i-v
characteristic, then switch can
be realized as shown

## Slide 15: Power Diode Overview
Diode
  Minority carrier device
  Passively controlled device
  Controlled by external circuitry
    Forward Bias to turn on
    Reverse Bias to turn off
  Relatively low on state conduction losses
  Turn-on is to charge the depletion capacitor across the pn-junction
  Turn-off is more complex.

## Slide 16: Diode Switching Characteristics Conventional

## Slide 17: Diode Switching Characteristics Conventional

## Slide 18: Diode Switching Characteristics Fast Recovery Type

## Slide 19: Types of Power Diodes
Standard recovery
Reverse time not specified, intended for 50/60 Hz
Fast recovery and ultra-fast recovery
Reverse recovery time and recovered charge specified
Intended for converter applications
Schottky diode
A majority carrier device
Essentially no recovered charge
Model with equilibrium I-V characteristic, in parallel with depletion region capacitance
Restricted to low voltage (few devices can block 110V or more)

## Slide 20: Diode Switching Characteristics Simulation-Dbreak
Time
10.0us
10.4us
10.8us
I(D1)
0A
0.5A
1.0A

## Slide 21: Diode Switching Characteristics Simulation-1N4002 General Purpose
Time
10.00us
10.25us
10.50us
10.75us
I(D1)
-80A
-40A
0A
40A
Time
10.700us
10.800us
10.624us
I(D1)
-40A
0A
-71A

## Slide 22: Diode Switching Characteristics Simulation-D1N4148-Fast Recovery
Time
10.0us
10.2us
10.4us
10.6us
10.8us
I(D1)
0A
0.5A
1.0A
Time
10.600us
10.620us
10.583us
I(D1)
-200mA
0A
200mA

## Slide 23: Survey of Commercial Power Diodes

## Slide 24: General Comments on Power Diodes
Inverse Relationship between Blocking voltage/Forward current and reverse recovery time/forward voltage drop
Generally, Diode turn on fast enough to be considered ideal
Device turn off generally considered ideal but can effect circuit operation
  Diode turn off means negative current needed to remove stored charge
    This charge removal is required for device turn off
    In some instances, this negative current and delay can have an effect on circuit operation
    Can result in inductive ringing (particularly when fast recovery used in an inductive environment)
When required, series diodes add to blocking capability

## Slide 25: Thyristors - Overview
Thyristors
  “Controlled diode”
  In off state, can block positive forward polarity voltage and thus not conduct
  Can be trigger into the on state by providing a short pulse of gate current provided that device is in forward blocking state
  Once device begins to conduct, it is LATCHED on and gate current can be removed

## Slide 26: Thyristors -SCR
Silicon Controlled Rectifier
  Once device begins to conduct, it is LATCHED on and gate current can be removed
  Cannot be turned off by active control (activity at gate)
  When current reduces and tries to go to negative, device turns off
  External circuit must reverse bias the SCR to achieve turn off
  After turn off, gate regains control allowing active turn on once the device is in forward blocking state

## Slide 27: Thyristors -SCR Symbol and Terminal Characteristics

## Slide 28: Thyristors -SCR Simulation
Time
0s
5ms
10ms
15ms
V(Gate)
0.5V
1.0V
-0.1V
SEL>>
I(Rload)
0A
0.5A
1.0A

## Slide 29: Commercial SCR Survey
Product | Package | Circuit | VDRM | IT(RMS)
ST180C04C0 | TO-200AA (A-Puk) | DISCRETE | 400 | 660
ST230C04C0 | TO-200AA (A-Puk) | DISCRETE | 400 | 780
ST280C04C0 | TO-200AA (A-Puk) | DISCRETE | 400 | 960
ST280C06C0 | TO-200AA (A-Puk) | DISCRETE | 600 | 960
ST280CH06C0 | TO-200AA (A-Puk) | DISCRETE | 600 | 1130
ST230C08C0 | TO-200AA (A-Puk) | DISCRETE | 800 | 780
ST180C08C0 | TO-200AA (A-Puk) | DISCRETE | 800 | 660
ST180C12C0 | TO-200AA (A-Puk) | DISCRETE | 1200 | 660
ST230C12C0 | TO-200AA (A-Puk) | DISCRETE | 1200 | 780
ST230C14C0 | TO-200AA (A-Puk) | DISCRETE | 1400 | 780
ST230C16C0 | TO-200AA (A-Puk) | DISCRETE | 1600 | 780
ST180C16C0 | TO-200AA (A-Puk) | DISCRETE | 1600 | 660
ST180C18C0 | TO-200AA (A-Puk) | DISCRETE | 1800 | 660
ST180C20C0 | TO-200AA (A-Puk) | DISCRETE | 2000 | 660

## Slide 30: General Comments on SCRs
Used to be device of choice for high power applications
SCR based Phase Controlled Rectifiers still common in three-phase industrial environment
A minority carrier device
SCR has highest blocking voltage and current carrying capabilities of all the semiconductor switches
Large reverse recovery current
Long carrier lifetimes allow low on state resistance but mean long turn off times
  Switching very slow
Newer designs rarely use SCRs unless very high power required
  Most newer designs use MOSFETs or IGBTs

## Slide 31: Thyristors -Triac
Triac
  “Back to back” SCR
  Bidirectional current flow, bidirectional voltage blocking
  Often used:
    AC waveform chopping: dimmers, soldering stations, controlled heating elements

## Slide 32: Thyristors -GTO
Gate Turn Off Thyristor
  Like SCR, once device begins to conduct, it is LATCHED on and gate current can be removed
  Unlike SCR, GTO can be turned off with a negative gate-cathode voltage (i.e. active turn off control)
  This negative gate current pulse can be short duration but must be large magnitude (~ .33 iA )
  A controlled switch like BJT/MOSFET but not suitable for inductive turn off
  Slow switching time (fs max ~10 kHz)

## Slide 33: Example 2.4 – Light Dimming - SCR
The average power applied to the light is varied to change its brightness.

## Slide 34: Example 2.4 – Light Dimming - Triac
The average power applied to the light is varied to change its brightness.

## Slide 35: BJT - Overview
Bipolar Junction Transistor
  A minority carrier device
  Current controlled
    Requires a continuous base current to remain in on (conducting) state
  Significant delays during turn off transition
  On-state resistance has negative temperature characteristic so device paralleling not always straightforward

## Slide 36: BJT Symbol and i-v Characteristics

## Slide 37: General Comments on BJT
BJT has been replaced by MOSFET in low-voltage (<500V) applications
BJT is being replaced by IGBT in applications at voltages above 500V
Design trade off between on-state losses and switching times
A minority-carrier device: compared with MOSFET, the BJT exhibits slower switching, but lower on-resistance at high voltages

## Slide 38: MOSFET Overview
Metal-Oxide-Semiconductor Field Effect Transistor
  A majority carrier device
  Voltage controlled
    Require continuous application of Gate to Source voltage to maintain on-state (conduction)
  No gate current flows except during transitions to charge and discharge gate capacitance
  Very short switching times
  On-state resistance has positive temperature coefficient so device paralleling simple

## Slide 39: MOSFET Symbol and i-v Characteristics

## Slide 40: Survey of Commercially Available MOSFETs

## Slide 41: General Comments on MOSFET
Majority carrier device: fast switching times
Typical switching frequencies: tens and hundreds of kHz
On state losses rise more rapidly with blocking voltage than in a comparable BJT
Easy to drive
The device of choice for blocking voltages less than 500V
1000V devices are available, but are useful only at low power levels (100W)
Generally, on state resistance most significant factor when selecting device

## Slide 42: IGBT Overview
Insulated Gate Bipolar Transistor
  Combination of BJT and MOSFET
    Like MOSFET, has high impedance gate which requires small charge to turn on
    Like BJT, small on state resistance even for devices with large blocking voltage ratings
  Can be designed to block negative voltages like thysistors

## Slide 43: IGBT Symbol and i-v Characteristics

## Slide 44: Survey of Commercially Available IGBTs

## Slide 45: General Comments on IGBT
Faster than comparable BJT, Slower than a comparable MOSFET
On state losses smaller than MOSFET and are comparable to BJT
Turn on time can be effected by rate of change of vgs
Most new designs in the industrial power electronics market use IGBTs for medium power applications

## Slide 46: Future Trends in Device Progress

## Slide 47: Device Comparison fs vs. Power

## Slide 48: Device Comparison Voltage vs. Power vs. Temperature

## Slide 49: Wide Band-Gap Semiconductors For Power Electronic
Si devices limited to operate below 200 C
Si power devices not suitable for very high switching speed (HSS)
Si power devices not suitable for very high voltage (HV) applications

## Slide 50: Applications fs vs. Power

## Slide 51: Comparison of the on-resistance (Ron) vs. Breakdown voltage

## Slide 52: fo vs. Size of Magnetic Component & Heat Sink

## Slide 53: Device Maximum Power